## Slide 1
Photo © 2010 NTNU Info / Geir Mogen
Quantum hacking
Lecture 12 in Quantum optics and communications (continuing education) course, 7 Dec 2022
vad1.com/lab
Vadim Makarov

## Slide 3: Implementation security of quantum communications
.Laws of physics & Model of equipment
Security proof
Hack
Integrate imperfection into security model
Formal certification: we need
standards and labs ecosystem

## Slide 4: Threat model
Kerckhoffs’ principle:
Il faut qu’il n’exige pas le secret, et qu’il puisse sans inconvénient tomber entre les mains de l’ennemi
A. Kerckhoffs, J. des Sciences Militaires 9, 5 (1883)
Everything about the system that is not explicitly secret is known to the enemy
Bob
Alice
Future technology
physically secure,
characteristics known
physically secure,
characteristics known

## Slide 5
Attack | Target component | Tested system
Distinguishability of decoy states | laser in Alice | 3 research systems
A. Huang et al., Phys. Rev. A 98, 012330 (2018) |  | 
Intersymbol interference | intensity modulator in Alice | research system
K. Yoshino et al., poster at QCrypt (2016) |  | 
Laser damage | any | 5 commercial & 1 research systems
V. Makarov et al., Phys. Rev. A 94, 030302 (2016); A. Huang et al., poster at QCrypt (2018) |  | 
Spatial efficiency mismatch | receiver optics | 2 research systems
M. Rau et al., IEEE J. Sel. Top. Quantum Electron. 21, 6600905 (2015); S. Sajeed et al., Phys. Rev. A 91, 062301 (2015) |  | 
Pulse energy calibration | classical watchdog detector | ID Quantique
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015) |  | 
Trojan-horse | phase modulator in Alice | SeQureNet
I. Khan et al., presentation at QCrypt (2014) |  | 
Trojan-horse | phase modulator in Bob | ID Quantique
N. Jain et al., New J. Phys. 16, 123030 (2014); S. Sajeed et al., Sci. Rep. 7, 8403 (2017) |  | 
Detector saturation | homodyne detector | SeQureNet
H. Qin, R. Kumar, R. Alleaume, Proc. SPIE 88990N (2013) |  | 
Shot-noise calibration | classical sync detector | SeQureNet
P. Jouguet, S. Kunz-Jacques, E. Diamanti, Phys. Rev. A 87, 062313 (2013) |  | 
Wavelength-selected PNS | intensity modulator | (theory)
M.-S. Jiang, S.-H. Sun, C.-Y. Li, L.-M. Liang, Phys. Rev. A 86, 032310 (2012) |  | 
Multi-wavelength | beamsplitter | research system
H.-W. Li et al., Phys. Rev. A 84, 062308 (2011) |  | 
Deadtime | single-photon detector | research system
H. Weier et al., New J. Phys. 13, 073024 (2011) |  | 
Channel calibration | single-photon detector | ID Quantique
N. Jain et al., Phys. Rev. Lett. 107, 110501 (2011) |  | 
Faraday-mirror | Faraday mirror | (theory)
S.-H. Sun, M.-S. Jiang, L.-M. Liang, Phys. Rev. A 83, 062331 (2011) |  | 
Detector control | single-photon detector | ID Quantique, MagiQ, research systems
I. Gerhardt et al., Nat. Commun. 2, 349 (2011); L. Lydersen et al., Nat. Photonics 4, 686 (2010) |  | 

## Slide 6: Example of vulnerability and countermeasures
Photon-number-splitting attack
C. Bennett, F. Bessette, G. Brassard, L. Salvail, J. Smolin, J. Cryptology 5, 3 (1992)
G. Brassard, N. Lütkenhaus, T. Mor, B. C. Sanders, Phys. Rev. Lett. 85, 1330 (2000)
N. Lütkenhaus, Phys. Rev. A 61, 052304 (2000)
S. Félix, N. Gisin, A. Stefanov, H. Zbinden, J. Mod. Opt. 48, 2009 (2001)
N. Lütkenhaus, M. Jahma, New J. Phys. 4, 44 (2002)
Decoy-state protocol
W.-Y. Hwang, Phys. Rev. Lett. 91, 057901 (2003)
SARG04 protocol
V. Scarani, A. Acín, G. Ribordy, N. Gisin, Phys. Rev. Lett. 92, 057901 (2004)
Distributed-phase-reference protocols
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. Lett. 89, 037902 (2002)
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. A. 68, 022317 (2003)
N. Gisin, G. Ribordy, H. Zbinden, D. Stucki, N. Brunner, V. Scarani, arXiv:quant-ph/0411022v1 (2004)
Laser
Attenuator

## Slide 7: Attenuated laser source
Attenuator
0 1 2 3
1
0.1
0.01
0.001
0 1 2 3
1
0.1
0.01
0.001
S. J. van Enk, C. A. Fuchs, arXiv:quant-ph/0111157
G
Laser diode

## Slide 8: Commercial QKD 1st generation (circa 2008) ID Quantique Cerberis system
www.swissquantum.com
QKD to another node (14 km)
QKD to another node (4 km)
Key manager
WDMs
Classical encryptors:
L2, 2 Gbit/s
L2, 10 Gbit/s
L3 VPN, 100 Mbit/s
Photo © 2010 Vadim Makarov

## Slide 9: True randomness?
ONE ONE ONE
ONE ONE ONE
ONE ONE ONE
Quantis
RNG
FPGA
Phase modulator in Bob
id Quantique Clavis2 (2008)
V/2
0
OK

## Slide 10: True randomness?
Quantis
RNG
FPGA
Phase modulator in Bob
Issue reported patched in 2010
Bob:
Alice:
id Quantique Clavis2 (2008)
V/2
0

## Slide 11: Do we trust the manufacturer?
Quantis RNG
*
Clicks
processed
Random
stream
Quantis RNG, Trojan-horsed :)
*
Clicks
processed
Random
stream
Switch
Memory with
pre-recorded
random
sequence
Many components in QKD system can be Trojan-horsed:
– access to secret information
– electrical power
– way to communicate outside or compromise security

## Slide 12: Quantis RNG: what’s inside?
G. Ribordy, O. Guinnard, US patent appl. US 2007/0127718 A1 (filed in 2006)
M. Petrov, I. Radchenko et al., EPJ Quantum Technol. 9, 17 (2022)
G
Debiasing
Output
4 Mbit/s
LED
820 nm
(40 nm FWHM)
20 MHz
20 µm

## Slide 13: ID Quantique Clavis2 QKD system
Alice
Bob
Photo © 2008 Vadim Makarov. Published with approval of ID Qiantique

## Slide 14: Double clicks
N. Lütkenhaus, Phys. Rev. A 59, 3301 (1999)
T. Tsurumaru & K. Tamaki, Phys. Rev. A 78, 032302 (2008)
– occur naturally because of detector dark counts, multi-photon pulses...
Discard them?
Proper treatment for double clicks: assign a random bit value.
Intercept-resend attack... with a twist:
Bob´
Alice´
Eve
100
photons
Alice
Bob:
Detects in
Eve’s basis:
single click
Detects in
conjugate basis:
double click,
discarded

## Slide 15: Trojan-horse attack
Alice
Line
Attenuator
Alice’s PC
Eve’s equipment
Phase modulator
– interrogating Alice’s phase modulator with powerful external pulses (can give Eve bit values directly)

## Slide 16: Trojan-horse attack for plug-and-play system
N. Gisin et al., Phys. Rev. A 73, 022320 (2006)
Alice
Bob
Eve gets back one photon  in principle, extracts 100% information

## Slide 17: Trojan-horse attack experiment
Laser
4% reflection
Vmod
OTDR
Out
In
Fine length adjustment
to get L1 = L2
L2
L1
Received OTDR pulse
Vmod, V
4.1
8.2
0
Variable attenuator
Alice
Phase modulator
Eve
A. Vakhitov et al., J. Mod. Opt. 48, 2023 (2001)

## Slide 18: Draft security standard @ ETSI: Trojan-horse in one-way system
M. Lucamarini et al., Phys. Rev. X 5, 031030 (2015)
Alice
Att.


Isolator(s)
BPF

## Slide 19: Attack example: avalanche photodetectors (APDs)
Ith
I
V
Linear mode
Geiger mode
Single photon
Breakdown
voltage Vbr
Popt
I
Quenching
Ith
Pth

## Slide 20: Faked-state attack in APD linear mode
Eve
L. Lydersen, C. Wiechers, C. Wittmann, D. Elser, J. Skaar, V. Makarov, Nat. Photonics 4, 686 (2010)
.Bob´
Bob
Bright
state
Identical bases & bit values
Classical post-processing
Listen, do same,
get same final key
.Alice´
Alice
Bob chooses same basis as Eve:
Bob chooses different basis:
“1
”
“0
”
t
t
I
th
I
th
t
t
I
th
I
th
I
0
I
1
I
0
I
1
“0”
“1
”
Click!

## Slide 21: Blinding APD with bright light
VAPD
Vbr
Vbias
t
0
Detector blind!
Zero dark count rate
Bias to APD
(Vbias)
VHV  40 V
Rbias
L. Lydersen, C. Wiechers, C. Wittmann, D. Elser, J. Skaar, V. Makarov, Nat. Photonics 4, 686 (2010)
No light
Eve applies CW light
0
1
2
Logic 0
Logic 1
Input
illumination
(mW)
Detector
output
−10
0
10
20
30
Time (ns)
−10
0
10
20
30
t
647 W
t
808 W
(never clicks)
(always clicks)
ID Quantique
Clavis2

## Slide 22: Proposed full eavesdropper
Basis
amplifier
Optical
Detection result
Bob´
Eve
Bob
Alice
Bit in
Basis
Alice´
Blinding laser
Note: Intercept-resend always breaks QKD security
M. Curty, M. Lewenstein, N. Lütkenhaus, Phys. Rev. Lett. 92, 217903 (2004)

## Slide 23: Eavesdropping 100% key on installed QKD line on campus of the National University of Singapore, July 4–5, 2009
S12
290 m of fiber
Alice
Bob
Eve
S15
S14
S13
Image © 2009 DigitalGlobe
I. Gerhardt, Q. Liu et al., Nat. Commun. 2, 349 (2011)

## Slide 24: Controlling superconducting nanowire single-photon detectors
L. Lydersen, M. K. Akhlaghi, A. H. Majedi, J. Skaar, V. Makarov, New J. Phys. 13, 113042 (2011)
M. G. Tanner, V. Makarov, R. H. Hadfield, Opt. Express 22, 6734 (2014)
1. Blind (latch)
2. Control
0
1
0
2
0
3
0
0
Time (ns)
Comparator input voltage (arb. units)
Normal single- photon click
14 mW pulse
7 mW pulse

## Slide 25: Countermeasures to detector attacks?

## Slide 26
Alice
Charlie (untrusted)
Bob
EPR
BSM
EPR
EPR
H.-K. Lo, M. Curty, B. Qi, Phys. Rev. Lett. 108, 130503 (2012)
Measurement-device-independent QKD
BSM
RNG
RNG
Mod.
Mod.
Photon
source
Photon
source
A. Ekert, Phys. Rev. Lett. 67, 661 (1991); C. H. Bennett et al., Phys. Rev. Lett. 68, 557 (1992)

## Slide 27: 3 ways to deal with an imperfection
Technical countermeasure that attempts to stop the attack
Make a scheme intrinsically insensitive to imperfection
Characterise imperfection, upper-bound partial information leakage, eliminate it by privacy amplification

## Slide 28: Distinguishability of source states
A. Huang, S.-H. Sun, Z. Liu, V. Makarov, Phys. Rev. A 98, 012330 (2018)
S. Nauerth et al., New J. Phys. 11, 065001 (2009)

## Slide 29: Distinguishability of source states
A. Huang, S.-H. Sun, Z. Liu, V. Makarov, Phys. Rev. A 98, 012330 (2018)

## Slide 30: Distinguishability of source states
A. Huang, S.-H. Sun, Z. Liu, V. Makarov, Phys. Rev. A 98, 012330 (2018)

## Slide 31: Certification of cryptographic tools
Government
Legal requirements
Approval
Certificate
System
Engineering documentation
Sale
Accredited lab
Manufacturer
Customer
National security agency

## Slide 32: Security audit
 | System | Report | Tests
 | Clavis3 | 2016 | –2018 interrupted
 | 40 MHz | 2016, 2018–19 | ongoing
(ООО Квантовые коммуникации) | Subcarrier scheme | 2018 | –2021
Certification standards are being drafted since 2019 in
Industry standards group in QKD
 | 312.5 MHz | 2022 | ongoing
S. Sajeed et al., Sci. Rep. 11, 5110 (2021)

## Slide 33: Example of initial analysis report
Missing a single security proof

## Slide 34
vad1.com/lab
Quantum hacking lab