## Slide 1
Quantum cryptography
Image from cover of
Physics World, March 1998
Quantum hacking lab
www.vad1.com/lab
Vadim Makarov
Lecture for CryptoWorks21, IQC, August 1, 2014

## Slide 2: Communication security you enjoy daily
Paying by credit card in a supermarket
Cell phone conversations, SMS
Email, chat, online calls
Secure browsing, shopping online
Cloud storage and communication between your devices
Software updates on your computer, phone, tablet
Online banking
Off-line banking: the bank needs to communicate internally
Electricity, water: the utility needs to communicate internally
Car keys
Electronic door keys
Government services (online or off-line)
Medical records at your doctor, hospital
Bypassing government surveillance and censorship

## Slide 3: Encryption and key distribution
Bob
Alice
RNG
Symmetric
cipher
Symmetric
cipher
Public (insecure) channel
Secret key
Secure channel
Messages
Messages
Encrypted messages
Quantum key distribution transmits secret key by sending quantum states over open channel.

## Slide 4: Public key cryptography
E.g., RSA (Rivest-Shamir-Adleman)
Elliptic-curve
Based on hypothesized one-way functions
Unexpected advances in classical cryptanalysis
Shor’s factorization algorithm for quantum computer
Time to build large quantum computer
Re-tool infrastructure
Encryption needs be secure
Time
What do we do here?
here?
P. W. Shor, SIAM J. Comput. 26, 1484 (1997)
Diagram courtesy M. Mosca

## Slide 5: Encryption and key distribution
Bob
Alice
Quantum key distribution transmits secret key by sending quantum states over open channel.
RNG
Symmetric
cipher
Symmetric
cipher
Public (insecure) channel
Secret key
Secure channel
Messages
Messages
Encrypted messages

## Slide 6: Quantum key distribution (QKD)
Retained bit sequence 1 – – 1 0 0 – 1 0 0 – 1 – 0
Bob’s measurement 1 0 0 1 0 0 1 1 0 0 0 1 0 0
Bob’s detection basis
Alice’s bit sequence 1 0 1 1 0 0 1 1 0 0 1 1 1 0
Light source
Alice
Bob
Diagonal detector basis
Horizontal-vertical detector basis
Diagonal polarization filters
Horizontal-vertical polarization filters
0
0
1
1
Image reprinted from article: W. Tittel, G. Ribordy & N. Gisin, “Quantum cryptography,” Physics World, March 1998

## Slide 7: Dealing with errors
Security proof:
Errors due to imperfections and Eve.
Must assume that all errors are due to Eve!
Error correction: standard classical protocols
Privacy amplification:
1 | 0 | 1 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0 | 0 | 0
1
1
0
0
1
0
1
raw key
random matrix
=
0
1
1
1
secure key
Error rate
Secure key generation rate

## Slide 8: Free-space QKD over 144 km
T. Schmitt-Manderbach et al., Phys. Rev. Lett. 98, 010504 (2007)

## Slide 9: Alice: Polarized photon source
S. Nauerth et al., New J. Phys. 11, 065001 (2009)

## Slide 10: Single-photon sources
Parametric down-conversion
Attenuated laser
Laser
Attenuator
Pump
laser
Non-linear
crystal
Heralding detector
0 1 2 3
1
0.1
0.01
0.001
0 1 2 3
1
0.1
0.01
0.001

## Slide 11: Bob: Polarization analyzer with single-photon detectors
50:50
PBS
PBS
APD,
+45°
l/2
22.5°
V
-45°
H
J. G. Rarity, P. C. M. Owens, P. R. Tapster, J. Mod. Opt. 41, 2435 (1994)

## Slide 12: Single-photon detectors
Avalanche photodiode
Photomultiplier tube
+Vbias > Vbr
Output
Photocathode
Dynodes
e
Images reprinted from: http://www.frankswebspace.org.uk/ScienceAndMaths/physics/physicsGCE/D1-5.htm; S. Cova et al., J. Mod. Opt. 51, 1267 (2004)

## Slide 13: Single-photon detectors
Transition-edge sensor
Superconducting nanowire
Al lead
W sensor
10 µm
Images reprinted from: R. Sobolewski et al., IEEE Trans. Appl. Supercond. 13, 1151 (2003)
Images reprinted from: B. Cabrera et al., Appl. Phys. Lett. 73, 735 (1998); A.J. Miller et al., Appl. Phys. Lett. 83, 791 (2003)

## Slide 14: Alice on La Palma
Photo © IQOQI Vienna

## Slide 15: Bob on Tenerife
Photo © IQOQI Vienna

## Slide 16: Quantum teleportation over 143 km
X.-S. Ma et al., Nature 489, 269 (2012)
Photo by Tobias Schmitt-Manderbach

## Slide 17: Polarization encoding
Retained bit sequence 1 – – 1 0 0 – 1 0 0 – 1 – 0
Bob’s measurement 1 0 0 1 0 0 1 1 0 0 0 1 0 0
Bob’s detection basis
Alice’s bit sequence 1 0 1 1 0 0 1 1 0 0 1 1 1 0
Light source
Alice
Bob
Diagonal detector basis
Horizontal-vertical detector basis
Diagonal polarization filters
Horizontal-vertical polarization filters
0
0
1
1
Image reprinted from article: W. Tittel, G. Ribordy & N. Gisin, “Quantum cryptography,” Physics World, March 1998

## Slide 18: Phase encoding, interferometric QKD channel
jA = – 45 or + 45 : 0
Detector bases:
jB = – 45 : X
jB = + 45 : Z
jA = +135 or – 135 : 1
j
A
Light
source
D
0
j
B
Alice
Bob
D
1
long
short
short
long
Transmission line

## Slide 19: Plug-and-play scheme
D. Stucki et al., New J. Phys. 4, 41 (2002)
Bob
Alice
j
A
j
B
PBS
BS
C
D0
D1
L
VOA
DL
FM
sync

## Slide 20: ID Quantique Clavis2 QKD system
Alice
Bob
Photo © 2008 Vadim Makarov. Published with approval of ID Qiantique

## Slide 21: Commercial QKD
17 km (fiber length)
14 km
4 km
www.swissquantum.com
ID Quantique Cerberis system (2010)
QKD to another node
(14 km)
QKD to another node
(4 km)
Key manager
WDMs
Classical encryptors:
L2, 2 Gbit/s
L2, 10 Gbit/s
L3 VPN, 100 Mbit/s
Photo © 2010 Vadim Makarov

## Slide 22: Trusted-node repeater
K1
QKD 1
K1
K2
QKD 2
K2
K1K2
Trusted node
User
User
K1
K1K2K2 = K1

## Slide 23: Trusted-node network
M. Sasaki et al., Opt. Express 19, 10387 (2011)

## Slide 24
Video ©2012 IQC / group of T. Jennewein

## Slide 25: Prototype single-photon detector (4-channel)
Photo © 2014 V. Makarov / IQC

## Slide 26
End of lecture 1

## Slide 27
Photo © 2010 NTNU Info / Geir Mogen
Quantum hacking
Vadim Makarov www.vad1.com/lab
Lecture for CryptoWorks21, IQC, August 1, 2014

## Slide 28: Security model of QKD
Alice
Bob
Secret key rate
0
0.11
0
1
QBER
R
.Laws of physics & Model of equipment
Security proof

## Slide 29: Security model of QKD
.Laws of physics & Model of equipment
Security proof
.Laws of physics & Model of equipment
Security proof
Hack
Integrate imperfection into security model

## Slide 30: Quantum hacking...
Discover vulnerabilities
Demonstrate attacks
Develop countermeasures
Eliminate imperfections

## Slide 31
Video ©2011 Marc Weber Tobias

## Slide 32
Video ©2011 Marc Weber Tobias

## Slide 33: Commercial QKD ID Quantique Cerberis system
www.swissquantum.com
QKD to another node (14 km)
QKD to another node (4 km)
Key manager
WDMs
Classical encryptors:
L2, 2 Gbit/s
L2, 10 Gbit/s
L3 VPN, 100 Mbit/s
Photo © 2010 Vadim Makarov

## Slide 34: True randomness?
ONE ONE ONE
ONE ONE ONE
ONE ONE ONE
Quantis
RNG
FPGA
Phase modulator in Bob
id Quantique Clavis2 (2008)
V/2
0
OK

## Slide 35: True randomness?
Quantis
RNG
FPGA
Phase modulator in Bob
Issue reported patched, as of January 2010
Bob:
Alice:
id Quantique Clavis2 (2008)
V/2
0

## Slide 36: Do we trust the manufacturer?
Quantis RNG
*
Clicks
processed
Random
stream
Quantis RNG, Trojan-horsed :)
*
Clicks
processed
Random
stream
Switch
Memory with
pre-recorded
random
sequence
Many components in QKD system can be Trojan-horsed:
– access to secret information
– electrical power
– way to communicate outside or compromise security

## Slide 37: ID Quantique Clavis2 QKD system
Alice
Bob
Photo © 2008 Vadim Makarov. Published with approval of ID Qiantique

## Slide 38: Quantis RNG: what’s inside?
G. Ribordy, O. Guinnard, US patent appl. US 2007/0127718 A1 (filed in 2006)
I. Radchenko et al., unpublished
G
Debiasing
Output
4 Mbit/s
LED
820 nm
(40 nm FWHM)
20 MHz
20 µm

## Slide 39: Double clicks
N. Lütkenhaus, Phys. Rev. A 59, 3301 (1999)
T. Tsurumaru & K. Tamaki, Phys. Rev. A 78, 032302 (2008)
– occur naturally because of detector dark counts, multi-photon pulses...
Discard them?
Proper treatment for double clicks: assign a random bit value.
Intercept-resend attack... with a twist:
Bob´
Alice´
Eve
100
photons
Alice
Bob:
Detects in
Eve’s basis:
single click
Detects in
conjugate basis:
double click,
discarded

## Slide 40: Trojan-horse attack
Alice
Line
Attenuator
Alice’s PC
Eve’s equipment
Phase modulator
– interrogating Alice’s phase modulator with powerful external pulses (can give Eve bit values directly)

## Slide 41: Trojan-horse attack experiment
Laser
4% reflection
Vmod
OTDR
Out
In
Fine length adjustment
to get L1 = L2
L2
L1
Received OTDR pulse
Vmod, V
4.1
8.2
0
Variable attenuator
Alice
Phase modulator
Eve
A. Vakhitov et al., J. Mod. Opt. 48, 2023 (2001)

## Slide 42
Photo © 2000 Vadim Makarov
Artem Vakhitov tunes up Eve’s setup

## Slide 43: Trojan-horse attack for plug-and-play system
N. Gisin et al., Phys. Rev. A 73, 022320 (2006)
Alice
Bob
Eve gets back one photon  in principle, extracts 100% information

## Slide 44: Countermeasures?
D. Stucki et al., New J. Phys. 4, 41 (2002)
Bob
Alice
j
A
j
B
PBS
BS
C
D0
D1
L
VOA
DL
FM
sync

## Slide 45: Countermeasures for plug-and-play system
Alice:
Bob: none
(one consequence: SARG protocol may be insecure)
1. Add narrowband
(200 GHz) filter
2. Add
CW
and
pulse energy
monitoring detectors
S. Sajeed, I. Radchenko, S. Kaiser, J.-P. Bourgoin, L. Monat, M. Legré, V. Makarov, unpublished
N. Jain, E. Anisimova, I. Khan, V. Makarov, Ch. Marquardt, G. Leuchs, arXiv:1406.5813

## Slide 46: Trojan-horse attack on Bob
Bob
j
B
PBS
BS
C
D0
D1
L
N. Jain, E. Anisimova, I. Khan, V. Makarov, Ch. Marquardt, G. Leuchs, arXiv:1406.5813

## Slide 47: Example of vulnerability and countermeasures
Photon-number-splitting attack
C. Bennett, F. Bessette, G. Brassard, L. Salvail, J. Smolin, J. Cryptology 5, 3 (1992)
G. Brassard, N. Lütkenhaus, T. Mor, B. C. Sanders, Phys. Rev. Lett. 85, 1330 (2000)
N. Lütkenhaus, Phys. Rev. A 61, 052304 (2000)
S. Félix, N. Gisin, A. Stefanov, H. Zbinden, J. Mod. Opt. 48, 2009 (2001)
N. Lütkenhaus, M. Jahma, New J. Phys. 4, 44 (2002)
Decoy-state protocol
W.-Y. Hwang, Phys. Rev. Lett. 91, 057901 (2003)
SARG04 protocol
V. Scarani, A. Acín, G. Ribordy, N. Gisin, Phys. Rev. Lett. 92, 057901 (2004)
Distributed-phase-reference protocols
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. Lett. 89, 037902 (2002)
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. A. 68, 022317 (2003)
N. Gisin, G. Ribordy, H. Zbinden, D. Stucki, N. Brunner, V. Scarani, arXiv:quant-ph/0411022v1 (2004)
Laser
Attenuator

## Slide 48
Attack | Target component | Tested system
Detector saturation | homodyne detector | SeQureNet
H. Qin, R. Kumar, R. Alleaume, presentation at QCrypt (2013) |  | 
Shot-noise calibration | sync detector | SeQureNet
P. Jouguet, S. Kunz-Jacques, E. Diamanti, Phys. Rev. A 87, 062313 (2013) |  | 
Wavelength-selected PNS | intensity modulator | (theory)
M.-S. Jiang, S.-H. Sun, C.-Y. Li, L.-M. Liang, Phys. Rev. A 86, 032310 (2012) |  | 
Multi-wavelength | beamsplitter | research syst.
H.-W. Li et al., Phys. Rev. A 84, 062308 (2011) |  | 
Deadtime | single-photon detector | research syst.
H. Weier et al., New J. Phys. 13, 073024 (2011) |  | 
Channel calibration | single-photon detector | ID Quantique
N. Jain et al., Phys. Rev. Lett. 107, 110501 (2011) |  | 
Faraday-mirror | Faraday mirror | (theory)
S.-H. Sun, M.-S. Jiang, L.-M. Liang, Phys. Rev. A 83, 062331 (2011) |  | 
Phase-remapping | phase modulator | ID Quantique
F. Xu, B. Qi, H.-K. Lo, New J. Phys. 12, 113026 (2010) |  | 
Detector control | single-photon detector | ID Quantique, MagiQ, research syst.
I. Gerhardt et al., Nat. Commun. 2, 349 (2011) L. Lydersen et al., Nat. Photonics 4, 686 (2010) |  | 
Time-shift | single-photon detector | ID Quantique
Y. Zhao et al., Phys. Rev. A 78, 042333 (2008) |  | 

## Slide 49
Attack | Target component | Tested system
Detector saturation | homodyne detector | SeQureNet
H. Qin, R. Kumar, R. Alleaume, presentation at QCrypt (2013) |  | 
Shot-noise calibration | sync detector | SeQureNet
P. Jouguet, S. Kunz-Jacques, E. Diamanti, Phys. Rev. A 87, 062313 (2013) |  | 
Wavelength-selected PNS | intensity modulator | (theory)
M.-S. Jiang, S.-H. Sun, C.-Y. Li, L.-M. Liang, Phys. Rev. A 86, 032310 (2012) |  | 
Multi-wavelength | beamsplitter | research syst.
H.-W. Li et al., Phys. Rev. A 84, 062308 (2011) |  | 
Deadtime | single-photon detector | research syst.
H. Weier et al., New J. Phys. 13, 073024 (2011) |  | 
Channel calibration | single-photon detector | ID Quantique
N. Jain et al., Phys. Rev. Lett. 107, 110501 (2011) |  | 
Faraday-mirror | Faraday mirror | (theory)
S.-H. Sun, M.-S. Jiang, L.-M. Liang, Phys. Rev. A 83, 062331 (2011) |  | 
Phase-remapping | phase modulator | ID Quantique
F. Xu, B. Qi, H.-K. Lo, New J. Phys. 12, 113026 (2010) |  | 
Detector control | single-photon detector | ID Quantique, MagiQ, research syst.
I. Gerhardt et al., Nat. Commun. 2, 349 (2011) L. Lydersen et al., Nat. Photonics 4, 686 (2010) |  | 
Time-shift | single-photon detector | ID Quantique
Y. Zhao et al., Phys. Rev. A 78, 042333 (2008) |  | 

## Slide 50: Attack example: avalanche photodetectors (APDs)
Ith
I
V
Linear mode
Geiger mode
Single photon
Breakdown
voltage Vbr
Popt
I
Quenching
Ith
Pth

## Slide 51: Faked-state attack in APD linear mode
Eve
L. Lydersen, C. Wiechers, C. Wittmann, D. Elser, J. Skaar, V. Makarov, Nat. Photonics 4, 686 (2010)
.Bob´
Bob
Bright
state
Identical bases & bit values
Classical post-processing
Listen, do same,
get same final key
.Alice´
Alice
Bob chooses same basis as Eve:
Bob chooses different basis:
“1
”
“0
”
t
t
I
th
I
th
t
t
I
th
I
th
I
0
I
1
I
0
I
1
“0”
“1
”
Click!

## Slide 52: Blinding APD with bright light
VAPD
Vbr
Vbias
t
0
Detector blind!
Zero dark count rate
Bias to APD
(Vbias)
VHV  40 V
Rbias
L. Lydersen, C. Wiechers, C. Wittmann, D. Elser, J. Skaar, V. Makarov, Nat. Photonics 4, 686 (2010)
No light
Eve applies CW light
0
0.5
1
1.5
2
-10
0
10
20
30
Logic 0
Logic 1
Time, ns
-10
0
10
20
30
Time, ns
t
647 W
t
808 W
(never clicks)
(always clicks)
Input
illumination,
mW
Detector
output
ID Quantique
Clavis2

## Slide 53: Lars Lydersen testing MagiQ Technologies QPN 5505
Photo © 2010 Vadim Makarov

## Slide 54: Proposed full eavesdropper
Basis
amplifier
Optical
Detection result
Bob´
Eve
Bob
Alice
Bit in
Basis
Alice´
Blinding laser

## Slide 55: Eavesdropping 100% key on installed QKD line on campus of the National University of Singapore, July 4–5, 2009
S12
290 m of fiber
Alice
Bob
S15
S14
S13
Image © 2009 DigitalGlobe
I. Gerhardt, Q. Liu et al., Nat. Commun. 2, 349 (2011)

## Slide 56: Entanglement-based QKD
M. P. Peloso et al., New J. Phys. 11, 045007 (2009)

## Slide 57: Eavesdropping 100% key on installed QKD line on campus of the National University of Singapore, July 4–5, 2009
S12
290 m of fiber
Alice
Bob
Eve
S15
S14
S13
Image © 2009 DigitalGlobe
I. Gerhardt, Q. Liu et al., Nat. Commun. 2, 349 (2011)

## Slide 58: Eve does not affect QKD performance
I. Gerhardt, Q. Liu, A. Lamas-Linares, J. Skaar, C. Kurtsiefer, V. Makarov, Nat. Commun. 2, 349 (2011)
Without eavesdropping
During eavesdropping
Raw key bit rate, s–1
QBER, %
Time, s
Time, s
0
100
200
300
0
1000
2000
3000
0
100
200
300
0
2
4
6
8
10

## Slide 59: Faking violation of Bell inequality
BS
/2
PBS
PBS
BS
/2
PBS
PBS
I. Gerhardt, Q. Liu et al., Phys. Rev. Lett. 107, 170404 (2011); N. Sultana, V. Makarov, unpublished
CHSH inequality:
Entangled photons:
Source of
entangled photons
Polarization
analyser B
Polarization
analyser A

## Slide 60: Faking violation of Bell inequality
BS
/2
PBS
PBS
BS
/2
PBS
PBS
I. Gerhardt, Q. Liu et al., Phys. Rev. Lett. 107, 170404 (2011); N. Sultana, V. Makarov, unpublished
CHSH inequality:
Entangled photons:
Passive basis choice: 100
Active basis choice:
Faked
state
generator
Faked
state
generator
Polarization
analyser B
Polarization
analyser A
Pattern generator

## Slide 61: Controlling superconducting nanowire single-photon detectors
L. Lydersen, M. K. Akhlaghi, A. H. Majedi, J. Skaar, V. Makarov, New J. Phys. 13, 113042 (2011)
M. G. Tanner, V. Makarov, R. H. Hadfield, arXiv:1305.5989
1. Blind (latch)
2. Control
0
1
0
2
0
3
0
0
Time, ns
Comparator input voltage, a.u.
Normal single- photon click
14 mW pulse
7 mW pulse

## Slide 62: Countermeasures to detector attacks
/ Eve
Software patch to randomly vary detector sensitivity
M. Legre, G. Ribordy, intl. patent appl. WO 2012/046135 A2 (filed in 2010)
Monitoring extra electrical parameters in detector
Z. L. Yuan, J. F. Dynes, A. J. Shields, Appl. Phys. Lett. 98, 231104 (2011)
...
Measurement-device-independent QKD
H.-K. Lo, M. Curty, B. Qi, Phys. Rev. Lett. 108, 130503 (2012)
Demonstration
in Calgary
Band-aid
Integrated into
security model
A. Rubenok et al., arXiv:1204.0738v2

## Slide 63: Responsible disclosure is important
Example: hacking commercial systems
ID Quantique got a detailed vulnerability report
  reaction: requested time, developed a patch
MagiQ Technologies got a detailed vulnerability report
  reaction: informed us that QPN 5505 is discontinued
Results presented orally at a scientific conference
Public disclosure in a journal paper
  L. Lydersen et al., Nat. Photonics 4, 686 (2010)
2009
2010
M. Legre, G. Ribordy, intl. patent appl. WO 2012/046135 A2 (filed in 2010)

## Slide 64: Can we eavesdrop on commercial systems?
ID Quantique’s Cerberis:
Dual key agreement
Photo © 2010 Vadim Makarov
QKD
QKD
PKI
PKI
Symmetric
cipher
Symmetric
cipher
RSA-2048
BB84
AES-256
Key
Key

## Slide 65: Some other topics in experimental quantum cryptography...
Continuous-variable QKD
Differential-phase-shift-keying protocols
Quantum repeaters
Device-independent QKD

## Slide 66
Quantum cryptography is a viable complement to aging classical cryptography methods
Quantum cryptography has implementation imperfections, too, and the research community handles this problem successfully

## Slide 67
Vadim Makarov www.vad1.com/lab