## Slide 1
Quantum cryptography
Image from cover of
Physics World, March 1998
Quantum hacking lab
www.vad1.com/lab
Vadim Makarov
Lecture at Phys 10 undergraduate seminar, University of Waterloo, September 30, 2014

## Slide 2: Communication security you enjoy daily
Paying by credit card in a supermarket
Cell phone conversations, SMS
Email, chat, online calls
Secure browsing, shopping online
Cloud storage and communication between your devices
Software updates on your computer, phone, tablet
Online banking
Off-line banking: the bank needs to communicate internally
Electricity, water: the utility needs to communicate internally
Car keys
Electronic door keys
Government services (online or off-line)
Medical records at your doctor, hospital
Bypassing government surveillance and censorship

## Slide 3: Encryption and key distribution
Bob
Alice
RNG
Symmetric
cipher
Symmetric
cipher
Public (insecure) channel
Secret key
Secure channel
Messages
Messages
Encrypted messages
Quantum key distribution transmits secret key by sending quantum states over open channel.

## Slide 4: Public key cryptography
E.g., RSA (Rivest-Shamir-Adleman)
Elliptic-curve
Based on hypothesized one-way functions
Unexpected advances in classical cryptanalysis
Shor’s factorization algorithm for quantum computer
Time to build large quantum computer
Re-tool infrastructure
Encryption needs be secure
Time
What do we do here?
here?
P. W. Shor, SIAM J. Comput. 26, 1484 (1997)
Diagram courtesy M. Mosca

## Slide 5: Encryption and key distribution
Bob
Alice
Quantum key distribution transmits secret key by sending quantum states over open channel.
RNG
Symmetric
cipher
Symmetric
cipher
Public (insecure) channel
Secret key
Secure channel
Messages
Messages
Encrypted messages

## Slide 6: Quantum key distribution (QKD)
Retained bit sequence 1 – – 1 0 0 – 1 0 0 – 1 – 0
Bob’s measurement 1 0 0 1 0 0 1 1 0 0 0 1 0 0
Bob’s detection basis
Alice’s bit sequence 1 0 1 1 0 0 1 1 0 0 1 1 1 0
Light source
Alice
Bob
Diagonal detector basis
Horizontal-vertical detector basis
Diagonal polarization filters
Horizontal-vertical polarization filters
0
0
1
1
Image reprinted from article: W. Tittel, G. Ribordy & N. Gisin, “Quantum cryptography,” Physics World, March 1998

## Slide 7: Free-space QKD over 144 km
T. Schmitt-Manderbach et al., Phys. Rev. Lett. 98, 010504 (2007)

## Slide 8: Phase encoding, interferometric QKD channel
jA = – 45 or + 45 : 0
Detector bases:
jB = – 45 : X
jB = + 45 : Z
jA = +135 or – 135 : 1
j
A
Light
source
D
0
j
B
Alice
Bob
D
1
long
short
short
long
Transmission line

## Slide 9: Commercial QKD
17 km (fiber length)
14 km
4 km
www.swissquantum.com
ID Quantique Cerberis system (2010)
QKD to another node
(14 km)
QKD to another node
(4 km)
Key manager
WDMs
Classical encryptors:
L2, 2 Gbit/s
L2, 10 Gbit/s
L3 VPN, 100 Mbit/s
Photo © 2010 Vadim Makarov

## Slide 10: Trusted-node repeater
K1
QKD 1
K1
K2
QKD 2
K2
K1K2
Trusted node
User
User
K1
K1K2K2 = K1

## Slide 11: Trusted-node network
M. Sasaki et al., Opt. Express 19, 10387 (2011)

## Slide 12
Video ©2012 IQC / group of T. Jennewein

## Slide 13: Security model of QKD
Alice
Bob
Secret key rate
0
0.11
0
1
QBER
R
.Laws of physics & Model of equipment
Security proof

## Slide 14: Security model of QKD
.Laws of physics & Model of equipment
Security proof
.Laws of physics & Model of equipment
Security proof
Hack
Integrate imperfection into security model

## Slide 15: Example of vulnerability and countermeasures
Photon-number-splitting attack
C. Bennett, F. Bessette, G. Brassard, L. Salvail, J. Smolin, J. Cryptology 5, 3 (1992)
G. Brassard, N. Lütkenhaus, T. Mor, B. C. Sanders, Phys. Rev. Lett. 85, 1330 (2000)
N. Lütkenhaus, Phys. Rev. A 61, 052304 (2000)
S. Félix, N. Gisin, A. Stefanov, H. Zbinden, J. Mod. Opt. 48, 2009 (2001)
N. Lütkenhaus, M. Jahma, New J. Phys. 4, 44 (2002)
Decoy-state protocol
W.-Y. Hwang, Phys. Rev. Lett. 91, 057901 (2003)
SARG04 protocol
V. Scarani, A. Acín, G. Ribordy, N. Gisin, Phys. Rev. Lett. 92, 057901 (2004)
Distributed-phase-reference protocols
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. Lett. 89, 037902 (2002)
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. A. 68, 022317 (2003)
N. Gisin, G. Ribordy, H. Zbinden, D. Stucki, N. Brunner, V. Scarani, arXiv:quant-ph/0411022v1 (2004)
Laser
Attenuator

## Slide 16
Attack | Target component | Tested system
Detector saturation | homodyne detector | SeQureNet
H. Qin, R. Kumar, R. Alleaume, presentation at QCrypt (2013) |  | 
Shot-noise calibration | sync detector | SeQureNet
P. Jouguet, S. Kunz-Jacques, E. Diamanti, Phys. Rev. A 87, 062313 (2013) |  | 
Wavelength-selected PNS | intensity modulator | (theory)
M.-S. Jiang, S.-H. Sun, C.-Y. Li, L.-M. Liang, Phys. Rev. A 86, 032310 (2012) |  | 
Multi-wavelength | beamsplitter | research syst.
H.-W. Li et al., Phys. Rev. A 84, 062308 (2011) |  | 
Deadtime | single-photon detector | research syst.
H. Weier et al., New J. Phys. 13, 073024 (2011) |  | 
Channel calibration | single-photon detector | ID Quantique
N. Jain et al., Phys. Rev. Lett. 107, 110501 (2011) |  | 
Faraday-mirror | Faraday mirror | (theory)
S.-H. Sun, M.-S. Jiang, L.-M. Liang, Phys. Rev. A 83, 062331 (2011) |  | 
Phase-remapping | phase modulator | ID Quantique
F. Xu, B. Qi, H.-K. Lo, New J. Phys. 12, 113026 (2010) |  | 
Detector control | single-photon detector | ID Quantique, MagiQ, research syst.
I. Gerhardt et al., Nat. Commun. 2, 349 (2011) L. Lydersen et al., Nat. Photonics 4, 686 (2010) |  | 
Time-shift | single-photon detector | ID Quantique
Y. Zhao et al., Phys. Rev. A 78, 042333 (2008) |  | 

## Slide 17: Eavesdropping 100% key on installed QKD line on campus of the National University of Singapore, July 4–5, 2009
S12
290 m of fiber
Alice
Bob
Eve
S15
S14
S13
Image © 2009 DigitalGlobe
I. Gerhardt, Q. Liu et al., Nat. Commun. 2, 349 (2011)

## Slide 18: Responsible disclosure is important
Example: hacking commercial systems
ID Quantique got a detailed vulnerability report
  reaction: requested time, developed a patch
MagiQ Technologies got a detailed vulnerability report
  reaction: informed us that QPN 5505 is discontinued
Results presented orally at a scientific conference
Public disclosure in a journal paper
  L. Lydersen et al., Nat. Photonics 4, 686 (2010)
2009
2010
M. Legre, G. Ribordy, intl. patent appl. WO 2012/046135 A2 (filed in 2010)

## Slide 19: Can we eavesdrop on commercial systems?
ID Quantique’s Cerberis:
Dual key agreement
Photo © 2010 Vadim Makarov
QKD
QKD
PKI
PKI
Symmetric
cipher
Symmetric
cipher
RSA-2048
BB84
AES-256
Key
Key

## Slide 20
Quantum cryptography is a viable complement to aging classical cryptography methods
Quantum cryptography has implementation imperfections, too, and the research community handles this problem successfully

## Slide 21
Vadim Makarov www.vad1.com/lab