## Slide 1
Talk at ETSI 2nd quantum-safe crypto workshop, Ottawa, 6–7 October 2014
Testing
quantum
crypto
Vadim Makarov
Image: street mural in Bucharest (fragment)
© 2013 Obie Platon, Irlo, Pisica Pătrată, Last, Spesh, Lumin

## Slide 2: Cryptography: classical vs. quantum
Based on...
Convenient to implement?
Forward secure?
Authenticate via PKI?
Loopholes in implementations?
Unproven mathematical assumptions
Laws of
physics
Yes
No
Yes
No
Yes
Yes
Yes

## Slide 4: Cryptography: classical vs. quantum
Based on...
Convenient to implement?
Forward secure?
Authenticate via PKI?
Loopholes in implementations?
Exploitable retroactively?
Unproven mathematical assumptions
Laws of
physics
Yes
No
Yes
No
Yes
Yes
Yes
Yes
No*
Sometimes
* Single exception: A. Lamas-Linares & C. Kurtsiefer, Opt. Express 15, 9388 (2007)

## Slide 5: Classical hacking vs. quantum hacking
Often, just a computer
($0 equipment)
Optics lab
($0.5M equipment)
Photo 2008 Joshua Delaughter CC-NC-BY 2.0
Photo ©2010 VG / Øyvind Nordahl Næss

## Slide 6: Security model of QKD
Alice
Bob
Secret key rate
0
0.11
0
1
QBER
R
.Laws of physics & Model of equipment
Security proof

## Slide 7: Security model of QKD
.Laws of physics & Model of equipment
Security proof
.Laws of physics & Model of equipment
Security proof
Hack
Integrate imperfection into security model

## Slide 8: Example of vulnerability and countermeasures
Photon-number-splitting attack
C. Bennett, F. Bessette, G. Brassard, L. Salvail, J. Smolin, J. Cryptology 5, 3 (1992)
G. Brassard, N. Lütkenhaus, T. Mor, B. C. Sanders, Phys. Rev. Lett. 85, 1330 (2000)
N. Lütkenhaus, Phys. Rev. A 61, 052304 (2000)
S. Félix, N. Gisin, A. Stefanov, H. Zbinden, J. Mod. Opt. 48, 2009 (2001)
N. Lütkenhaus, M. Jahma, New J. Phys. 4, 44 (2002)
Decoy-state protocol
W.-Y. Hwang, Phys. Rev. Lett. 91, 057901 (2003)
SARG04 protocol
V. Scarani, A. Acín, G. Ribordy, N. Gisin, Phys. Rev. Lett. 92, 057901 (2004)
Distributed-phase-reference protocols
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. Lett. 89, 037902 (2002)
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. A. 68, 022317 (2003)
N. Gisin, G. Ribordy, H. Zbinden, D. Stucki, N. Brunner, V. Scarani, arXiv:quant-ph/0411022v1 (2004)
Laser
Attenuator

## Slide 9
Attack | Target component | Tested system
Pulse energy calibration | classical watchdog detector | ID Quantique
S. Sajeed et al., presentation at QCrypt (2014) |  | 
Trojan-horse | phase modulator in Alice | SeQureNet
I. Khan et al., presentation at QCrypt (2014) |  | 
Trojan-horse | phase modulator in Bob | ID Quantique*
N. Jain et al., arXiv:1406.5813 |  | 
Detector saturation | homodyne detector | SeQureNet
H. Qin, R. Kumar, R. Alleaume, presentation at QCrypt (2013) |  | 
Shot-noise calibration | classical sync detector | SeQureNet
P. Jouguet, S. Kunz-Jacques, E. Diamanti, Phys. Rev. A 87, 062313 (2013) |  | 
Wavelength-selected PNS | intensity modulator | (theory)
M.-S. Jiang, S.-H. Sun, C.-Y. Li, L.-M. Liang, Phys. Rev. A 86, 032310 (2012) |  | 
Multi-wavelength | beamsplitter | research syst.
H.-W. Li et al., Phys. Rev. A 84, 062308 (2011) |  | 
Deadtime | single-photon detector | research syst.
H. Weier et al., New J. Phys. 13, 073024 (2011) |  | 
Channel calibration | single-photon detector | ID Quantique
N. Jain et al., Phys. Rev. Lett. 107, 110501 (2011) |  | 
Faraday-mirror | Faraday mirror | (theory)
S.-H. Sun, M.-S. Jiang, L.-M. Liang, Phys. Rev. A 83, 062331 (2011) |  | 
Detector control | single-photon detector | ID Quantique, MagiQ, research syst.
I. Gerhardt et al., Nat. Commun. 2, 349 (2011); L. Lydersen et al., Nat. Photonics 4, 686 (2010) |  | 
Phase-remapping | phase modulator in Alice | ID Quantique*
F. Xu, B. Qi, H.-K. Lo, New J. Phys. 12, 113026 (2010) |  | 
Time-shift | single-photon detector | ID Quantique
Y. Zhao et al., Phys. Rev. A 78, 042333 (2008) |  | 
* Attack did not break security of the tested system, but may be applicable to a different implementation. |  | 

## Slide 10
Attack | Target component | Tested system
Pulse energy calibration | classical watchdog detector | ID Quantique
S. Sajeed et al., presentation at QCrypt (2014) |  | 
Trojan-horse | phase modulator in Alice | SeQureNet
I. Khan et al., presentation at QCrypt (2014) |  | 
Trojan-horse | phase modulator in Bob | ID Quantique*
N. Jain et al., arXiv:1406.5813 |  | 
Detector saturation | homodyne detector | SeQureNet
H. Qin, R. Kumar, R. Alleaume, presentation at QCrypt (2013) |  | 
Shot-noise calibration | classical sync detector | SeQureNet
P. Jouguet, S. Kunz-Jacques, E. Diamanti, Phys. Rev. A 87, 062313 (2013) |  | 
Wavelength-selected PNS | intensity modulator | (theory)
M.-S. Jiang, S.-H. Sun, C.-Y. Li, L.-M. Liang, Phys. Rev. A 86, 032310 (2012) |  | 
Multi-wavelength | beamsplitter | research syst.
H.-W. Li et al., Phys. Rev. A 84, 062308 (2011) |  | 
Deadtime | single-photon detector | research syst.
H. Weier et al., New J. Phys. 13, 073024 (2011) |  | 
Channel calibration | single-photon detector | ID Quantique
N. Jain et al., Phys. Rev. Lett. 107, 110501 (2011) |  | 
Faraday-mirror | Faraday mirror | (theory)
S.-H. Sun, M.-S. Jiang, L.-M. Liang, Phys. Rev. A 83, 062331 (2011) |  | 
Detector control | single-photon detector | ID Quantique, MagiQ, research syst.
I. Gerhardt et al., Nat. Commun. 2, 349 (2011); L. Lydersen et al., Nat. Photonics 4, 686 (2010) |  | 
Phase-remapping | phase modulator in Alice | ID Quantique*
F. Xu, B. Qi, H.-K. Lo, New J. Phys. 12, 113026 (2010) |  | 
Time-shift | single-photon detector | ID Quantique
Y. Zhao et al., Phys. Rev. A 78, 042333 (2008) |  | 
* Attack did not break security of the tested system, but may be applicable to a different implementation. |  | 

## Slide 11: Intercept-resend attack with Bob’s detector control
L. Lydersen et al., Nat. Photonics 4, 686 (2010)
V. Makarov, New J. Phys. 11, 065003 (2009)
V. Makarov, D. R. Hjelme, J. Mod. Opt. 52, 691 (2005)
Bob
Eve
.Bob´
Alice
Bright-light controller
Now-classical
detectors
Repeat what I have detected!
(blinded)
Identical bases & bit values

## Slide 12: Countermeasures to detector attacks
Monitoring extra electrical parameters in detector
Z. L. Yuan, J. F. Dynes, A. J. Shields, Appl. Phys. Lett. 98, 231104 (2011)
Randomly varying detector sensitivity
M. Legre, G. Robordy, Intl. patent appl. WO 2012/046135 A2 (filed in 2010) C. C. W. Lim et al., arXiv:1408.6398
Measurement-device-independent QKD
H.-K. Lo, M. Curty, B. Qi, Phys. Rev. Lett. 108, 130503 (2012)
Technical
Integrated into
security model

## Slide 13: Monitoring extra electrical parameters in detector (Toshiba)
Z. L. Yuan, J. F. Dynes, A. J. Shields, Appl. Phys. Lett. 98, 231104 (2011);
L. Lydersen, V. Makarov, J. Skaar, Appl. Phys. Lett. 99, 196101 (2011).
Z. L. Yuan, J. F. Dynes, A. J. Shields, Nat. Photonics 4, 800 (2010); L. Lydersen et al., ibid. 801.
Bias
tee
Rbias
50 
Vbias
Gate
1 Rbias = 0
3 Monitor Ibias for “anomalously high” values
2 Comparator threshold just above capacitive signal
3.5 ns
4 Accept clicks in narrow time window
Capacitive signal
Avalanche
Gain modulation @ Rbias = 0

## Slide 14: I: Can we test your detector?
Toshiba: No.
I: Why not?
Toshiba: Still no.
Chinese way: build a copy and hack it.
M.-S. Jiang et al., Phys. Rev. A 88, 062335 (2013)

## Slide 15: Randomly varying detector sensitivity (ID Quantique)
C. C. W. Lim et al., arXiv:1408.6398
M. Legre, G. Robordy, Intl. patent appl. WO 2012/046135 A2 (filed in 2010)
VAPD
Click
Click
VAPD
Click
Click
Alarm!

## Slide 16: Countermeasures to detector attacks
Monitoring extra electrical parameters in detector
Z. L. Yuan, J. F. Dynes, A. J. Shields, Appl. Phys. Lett. 98, 231104 (2011)
Randomly varying detector sensitivity
M. Legre, G. Robordy, Intl. patent appl. WO 2012/046135 A2 (filed in 2010) C. C. W. Lim et al., arXiv:1408.6398
Measurement-device-independent QKD
H.-K. Lo, M. Curty, B. Qi, Phys. Rev. Lett. 108, 130503 (2012)
Technical
Integrated into
security model
BSM
RNG
RNG
Mod.
Mod.
Photon
source
Photon
source
Alice
Charlie
(untrusted)
Bob
publicly announces BSM result

## Slide 17: Measurement-device-independent QKD: experiments
Calgary, 28 km
A. Rubenok et al., arXiv:1204.0738v2
Rio de Janeiro, 17 km
T. Ferreira da Silva et al., Phys. Rev. A 88, 052303 (2013)
Toronto, 10 km
Z. Tang et al., Phys. Rev. Lett. 112, 190503 (2014)
Hefei, 200 km
Y.-L. Tang et al., arXiv:1407.8012

## Slide 18: Responsible disclosure is important
Example: hacking commercial systems
ID Quantique got a detailed vulnerability report
  reaction: requested time, developed a patch
MagiQ Technologies got a detailed vulnerability report
  reaction: informed us that QPN 5505 is discontinued
Results presented orally at a scientific conference
Public disclosure in a journal paper
  L. Lydersen et al., Nat. Photonics 4, 686 (2010)
2009
2010
M. Legre, G. Ribordy, intl. patent appl. WO 2012/046135 A2 (filed in 2010)

## Slide 19: Dual key agreement
Photo © 2010 Vadim Makarov
QKD
QKD
PKI
PKI
Symmetric
cipher
Symmetric
cipher
RSA-2048
BB84
AES-256
Key
Key
www.swissquantum.com
ID Quantique Cerberis system (2010)
Certified

## Slide 20
Vadim Makarov www.vad1.com/lab