## Slide 1
Photo © 2010 NTNU Info / Geir Mogen
Quantum hacking
Vadim Makarov www.vad1.com/lab
Lecture at ID Quantique 8th winter school on quantum cybersecurity, Les Diablerets, January 16–21, 2016

## Slide 2: Security model of QKD
Alice
Bob
Secret key rate
0
0.11
0
1
QBER
R
.Laws of physics & Model of equipment
Security proof

## Slide 3: Security model of QKD
.Laws of physics & Model of equipment
Security proof
.Laws of physics & Model of equipment
Security proof
Hack
Integrate imperfection into security model

## Slide 4: Example of vulnerability and countermeasures
Photon-number-splitting attack
C. Bennett, F. Bessette, G. Brassard, L. Salvail, J. Smolin, J. Cryptology 5, 3 (1992)
G. Brassard, N. Lütkenhaus, T. Mor, B. C. Sanders, Phys. Rev. Lett. 85, 1330 (2000)
N. Lütkenhaus, Phys. Rev. A 61, 052304 (2000)
S. Félix, N. Gisin, A. Stefanov, H. Zbinden, J. Mod. Opt. 48, 2009 (2001)
N. Lütkenhaus, M. Jahma, New J. Phys. 4, 44 (2002)
Decoy-state protocol
W.-Y. Hwang, Phys. Rev. Lett. 91, 057901 (2003)
SARG04 protocol
V. Scarani, A. Acín, G. Ribordy, N. Gisin, Phys. Rev. Lett. 92, 057901 (2004)
Distributed-phase-reference protocols
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. Lett. 89, 037902 (2002)
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. A. 68, 022317 (2003)
N. Gisin, G. Ribordy, H. Zbinden, D. Stucki, N. Brunner, V. Scarani, arXiv:quant-ph/0411022v1 (2004)
Laser
Attenuator

## Slide 5
Attack | Target component | Tested system
Laser damage | any | ID Quantique, research system
V. Makarov et al., arXiv:1510.03148 |  | 
Spatial efficiency mismatch | receiver optics | research system
M Rau et al., IEEE J. Quantum Electron. 21, 6600905 (2015); S. Sajeed et al., Phys. Rev. A 91, 062301 (2015) |  | 
Pulse energy calibration | classical watchdog detector | ID Quantique
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015) |  | 
Trojan-horse | phase modulator in Alice | SeQureNet
I. Khan et al., presentation at QCrypt (2014) |  | 
Trojan-horse | phase modulator in Bob | ID Quantique*
N. Jain et al., New J. Phys. 16, 123030 (2014) |  | 
Detector saturation | homodyne detector | SeQureNet
H. Qin, R. Kumar, R. Alleaume, Proc. SPIE 88990N (2013) |  | 
Shot-noise calibration | classical sync detector | SeQureNet
P. Jouguet, S. Kunz-Jacques, E. Diamanti, Phys. Rev. A 87, 062313 (2013) |  | 
Wavelength-selected PNS | intensity modulator | (theory)
M.-S. Jiang, S.-H. Sun, C.-Y. Li, L.-M. Liang, Phys. Rev. A 86, 032310 (2012) |  | 
Multi-wavelength | beamsplitter | research system
H.-W. Li et al., Phys. Rev. A 84, 062308 (2011) |  | 
Deadtime | single-photon detector | research system
H. Weier et al., New J. Phys. 13, 073024 (2011) |  | 
Channel calibration | single-photon detector | ID Quantique
N. Jain et al., Phys. Rev. Lett. 107, 110501 (2011) |  | 
Faraday-mirror | Faraday mirror | (theory)
S.-H. Sun, M.-S. Jiang, L.-M. Liang, Phys. Rev. A 83, 062331 (2011) |  | 
Detector control | single-photon detector | ID Quantique, MagiQ, research system
I. Gerhardt et al., Nat. Commun. 2, 349 (2011); L. Lydersen et al., Nat. Photonics 4, 686 (2010) |  | 
* Attack did not break security of the tested system, but may be applicable to a different implementation. |  | 

## Slide 6: Commercial QKD ID Quantique Cerberis system
www.swissquantum.com
QKD to another node (14 km)
QKD to another node (4 km)
Key manager
WDMs
Classical encryptors:
L2, 2 Gbit/s
L2, 10 Gbit/s
L3 VPN, 100 Mbit/s
Photo © 2010 Vadim Makarov

## Slide 7: True randomness?
ONE ONE ONE
ONE ONE ONE
ONE ONE ONE
Quantis
RNG
FPGA
Phase modulator in Bob
id Quantique Clavis2 (2008)
V/2
0
OK

## Slide 8: True randomness?
Quantis
RNG
FPGA
Phase modulator in Bob
Issue reported patched in 2010
Bob:
Alice:
id Quantique Clavis2 (2008)
V/2
0

## Slide 9: Do we trust the manufacturer?
Quantis RNG
*
Clicks
processed
Random
stream
Quantis RNG, Trojan-horsed :)
*
Clicks
processed
Random
stream
Switch
Memory with
pre-recorded
random
sequence
Many components in QKD system can be Trojan-horsed:
– access to secret information
– electrical power
– way to communicate outside or compromise security

## Slide 10: ID Quantique Clavis2 QKD system
Alice
Bob
Photo © 2008 Vadim Makarov. Published with approval of ID Qiantique

## Slide 11: Double clicks
N. Lütkenhaus, Phys. Rev. A 59, 3301 (1999)
T. Tsurumaru & K. Tamaki, Phys. Rev. A 78, 032302 (2008)
– occur naturally because of detector dark counts, multi-photon pulses...
Discard them?
Proper treatment for double clicks: assign a random bit value.
Intercept-resend attack... with a twist:
Bob´
Alice´
Eve
100
photons
Alice
Bob:
Detects in
Eve’s basis:
single click
Detects in
conjugate basis:
double click,
discarded

## Slide 12: Trojan-horse attack
Alice
Line
Attenuator
Alice’s PC
Eve’s equipment
Phase modulator
– interrogating Alice’s phase modulator with powerful external pulses (can give Eve bit values directly)

## Slide 13: Trojan-horse attack experiment
Laser
4% reflection
Vmod
OTDR
Out
In
Fine length adjustment
to get L1 = L2
L2
L1
Received OTDR pulse
Vmod, V
4.1
8.2
0
Variable attenuator
Alice
Phase modulator
Eve
A. Vakhitov et al., J. Mod. Opt. 48, 2023 (2001)

## Slide 14: Artem Vakhitov tunes up Eve’s setup
Photo © 2000 Vadim Makarov

## Slide 15: Trojan-horse attack for plug-and-play system
N. Gisin et al., Phys. Rev. A 73, 022320 (2006)
Alice
Bob
Eve gets back one photon  in principle, extracts 100% information

## Slide 16: Countermeasures?
D. Stucki et al., New J. Phys. 4, 41 (2002)
Bob
Alice
j
A
j
B
PBS
BS
C
D0
D1
L
VOA
DL
FM
sync

## Slide 17: Countermeasures for plug-and-play system
Alice:
Bob: none
(one consequence: SARG protocol may be insecure)
1. Add narrowband
(1 nm) filter
2. Add
CW
and
pulse energy
monitoring detectors
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015)
N. Jain et al., New J. Phys. 16, 123030 (2014)

## Slide 18: Pulse-energy-monitoring detector
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015)
Theory:
Implementation:

## Slide 19: Pulse-energy-monitoring detector
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015)
Theory:
Attack:

## Slide 20: Trojan-horse attack on Bob
Bob
j
B
PBS
BS
C
D0
D1
L
N. Jain et al., New J. Phys. 16, 123030 (2014)
 −50 dB
−57 dB
4 photons
2106 photons
readout
j
B

## Slide 21
End of lecture 1

## Slide 22: Attack example: avalanche photodetectors (APDs)
Ith
I
V
Linear mode
Geiger mode
Single photon
Breakdown
voltage Vbr
Popt
I
Quenching
Ith
Pth

## Slide 23: Faked-state attack in APD linear mode
Eve
L. Lydersen, C. Wiechers, C. Wittmann, D. Elser, J. Skaar, V. Makarov, Nat. Photonics 4, 686 (2010)
.Bob´
Bob
Bright
state
Identical bases & bit values
Classical post-processing
Listen, do same,
get same final key
.Alice´
Alice
Bob chooses same basis as Eve:
Bob chooses different basis:
“1
”
“0
”
t
t
I
th
I
th
t
t
I
th
I
th
I
0
I
1
I
0
I
1
“0”
“1
”
Click!

## Slide 24: Blinding APD with bright light
VAPD
Vbr
Vbias
t
0
Detector blind!
Zero dark count rate
Bias to APD
(Vbias)
VHV  40 V
Rbias
L. Lydersen, C. Wiechers, C. Wittmann, D. Elser, J. Skaar, V. Makarov, Nat. Photonics 4, 686 (2010)
No light
Eve applies CW light
0
0.5
1
1.5
2
-10
0
10
20
30
Logic 0
Logic 1
Time, ns
-10
0
10
20
30
Time, ns
t
647 W
t
808 W
(never clicks)
(always clicks)
Input
illumination,
mW
Detector
output
ID Quantique
Clavis2

## Slide 25: Proposed full eavesdropper
Basis
amplifier
Optical
Detection result
Bob´
Eve
Bob
Alice
Bit in
Basis
Alice´
Blinding laser

## Slide 26: Eavesdropping 100% key on installed QKD line on campus of the National University of Singapore, July 4–5, 2009
S12
290 m of fiber
Alice
Bob
Eve
S15
S14
S13
Image © 2009 DigitalGlobe
I. Gerhardt, Q. Liu et al., Nat. Commun. 2, 349 (2011)

## Slide 27: Controlling superconducting nanowire single-photon detectors
L. Lydersen, M. K. Akhlaghi, A. H. Majedi, J. Skaar, V. Makarov, New J. Phys. 13, 113042 (2011)
M. G. Tanner, V. Makarov, R. H. Hadfield, arXiv:1305.5989
1. Blind (latch)
2. Control
0
1
0
2
0
3
0
0
Time, ns
Comparator input voltage, a.u.
Normal single- photon click
14 mW pulse
7 mW pulse

## Slide 28: Countermeasures to detector attacks?

## Slide 29: Perfect countermeasure to detector attacks
H.-K. Lo, M. Curty, B. Qi, Phys. Rev. Lett. 108, 130503 (2012)
Measurement-device-independent QKD
Alice
Charlie (untrusted)
Bob
Bell-state measurement
RNG
RNG
Mod.
Mod.
Photon
source
Photon
source

## Slide 30: Industrial countermeasure (ID Quantique)
A. Huang et al., arXiv:1601.00993
Lim et al. upload a preprint about countermeasure arXiv:1408.6398
2009-10-22
Report about detector blinding attack sent to IDQ
2010-10-08
IDQ applies for a patent on randomization of detector efficiency as a countermeasure
2014-08-27
2014-11-18
2015-04-17
Implementation of countermeasure delivered by IDQ to our lab (firmware update for Clavis2)
Testing report sent to IDQ proposing a modified attack that works
2004-11-10
First commercial Clavis1 system is shipped to a customer
Testing report sent to IDQ showing full implementation of
countermeasure to be unreliable
2015-12-21

## Slide 31: Randomly varying detector efficiency
M. Legre, G. Robordy, Intl. patent appl. WO 2012/046135 A2 (filed in 2010)
VAPD
Click
Click
VAPD
Click
Click
Alarm!

## Slide 32: Oscillograms at comparator input
A. Huang et al., arXiv:1601.00993

## Slide 33: Full two-efficiency-level countermeasure
A. Huang et al., arXiv:1601.00993
C. C. W. Lim et al., IEEE J. Sel. Top. Quantum Electron. 21, 6601305 (2015)
M. Legre, G. Robordy, Intl. patent appl. WO 2012/046135 A2 (filed in 2010)
VAPD
η
η
η/2
η
η
η/2
η
0
0

## Slide 34: Anqi Huang tests countermeasure in Clavis2
Photo © 2015 Vadim Makarov

## Slide 35: Security model of QKD
.Laws of physics & Model of equipment
Security proof
Hack
Integrate imperfection into security model

## Slide 36: Laser damage!
.Laws of physics & Model of equipment
Security proof
Who knows what...?
Physical access to equipment
Limits on physical security

## Slide 37: Laser damage in commercial QKD system Clavis2
V. Makarov et al., arXiv:1510.03148
0
Power
t
~25 s

## Slide 38: InGaAs p-i-n photodiode Dpulse (JDSU EPM 605LL)
V. Makarov et al., arXiv:1510.03148
Reproducible
(repeated with 3 samples)

## Slide 39: QKD system log
V. Makarov et al., arXiv:1510.03148

## Slide 40
Photo © 2015 Vadim Makarov

## Slide 41: Can we eavesdrop on commercial systems?
ID Quantique’s Cerberis:
Dual key agreement
Photo © 2010 Vadim Makarov
QKD
QKD
PKI
PKI
Symmetric
cipher
Symmetric
cipher
RSA-2048
BB84
AES-256
Key
Key

## Slide 42: Kerckhoffs’ principle
Il faut qu’il n’exige pas le secret, et qu’il puisse sans inconvénient tomber entre les mains de l’ennemi
A. Kerckhoffs, J. des Sciences Militaires IX, 5 (1883)
Everything about the system that is not explicitly secret is known to the enemy
Bob
Alice
Future technology
characteristics known
characteristics known

## Slide 43: Eavesdropping in real life?
Bob
Alice
Future technology
characteristics known
characteristics known
Bob
Alice
Implemented
characteristics measured
characteristics measured
I. Gerhardt et al., Nat. Commun. 2, 349 (2011)
Bob
Alice
Today’s technology
(modeled)
characteristics measured
characteristics measured
Many papers
Bob
Alice
Implemented
no access
no access
Not yet :)
Bob
Alice
Future technology
characteristics known
characteristics known
Many papers
Future technology