## Slide 1
Implementation of quantum communication: Lecture 3
Vadim Makarov www.vad1.com/lab
Course QIC 891, University of Waterloo, August 3, 2016
Photo © 2008 Vadim Makarov. Published with approval of ID Qiantique

## Slide 2: Outline of the rest of this course
Summary of communication security, quantum key distribution, trusted-repeater networks
Security model of QKD, side-channels in implementations
Examples of side-channel attacks, countermeasures, testing countermeasures
Conclusion & discussion
(optional) Lab visit
August 12 3

## Slide 3: Communication security you enjoy daily
Paying by credit card in a supermarket
Cell phone conversations, SMS
Email, chat, online calls
Secure browsing, shopping online
Cloud storage and communication between your devices
Software updates on your computer, phone, tablet
Online banking
Off-line banking: the bank needs to communicate internally
Electricity, water: the utility needs to communicate internally
Car keys, electronic door keys, access control
Government services (online or off-line)
Medical records at your doctor, hospital
Bypassing government surveillance and censorship
Security cameras, industrial automation, military, spies...

## Slide 4: A (very) brief history of cryptography
 |  |  |  |  | Broken? |  | 
Monoalphabetic cipher |  | invented ~50 BC (J. Caesar) |  |  | ~850 (Al-Kindi) |  | 
Nomenclators (code books) |  | ~1400 – ~1800 |  |  |  |  | 
Polyalphabetic (Vigenère) |  | 1553 – ~1900 |  |  | 1863 (F. W. Kasiski) |  | 
··· |  |  |  |  |  |  | 
One-time pad |  | invented 1918 (G. Vernam) |  |  | impossible (C. Shannon 1949) |  | 
Polyalphabetic electromechanical (Enigma, Purple, etc.) |  | 1920s – 1970s |  |  |  |  | 
··· |  |  |  |  |  |  | 
DES |  | 1977 – 2005 |  |  | 1998: 56 h (EFF) |  | 
Public-key crypto (RSA, elliptic-curve) |  |  | 1977 – |  | will be once we have q. computer (P. Shor 1994) |  | 
AES |  | 2001 – |  |  | ? |  | 
Quantum cryptography | invented 1984, in development |  |  |  |  | impossible | 
Public-key crypto (‘quantum-safe’) |  | in development |  |  | ? |  | 
 |  |  |  |  | Broken? |  | 
Monoalphabetic cipher |  | invented ~50 BC (J. Caesar) |  |  | ~850 (Al-Kindi) |  | 
Nomenclators (code books) |  | ~1400 – ~1800 |  |  |  |  | 
Polyalphabetic (Vigenère) |  | 1553 – ~1900 |  |  | 1863 (F. W. Kasiski) |  | 
··· |  |  |  |  |  |  | 
Polyalphabetic electromechanical (Enigma, Purple, etc.) |  | 1920s – 1970s |  |  |  |  | 
··· |  |  |  |  |  |  | 
DES |  | 1977 – 2005 |  |  | 1998: 56 h (EFF) |  | 
Public-key crypto (RSA, elliptic-curve) |  |  | 1977 – |  | will be once we have q. computer (P. Shor 1994) |  | 
AES |  | 2001 – |  |  | ? |  | 
Public-key crypto (‘quantum-safe’) |  | in development |  |  | ? |  | 


## Slide 5: One-time pad
Bob
Alice
Random
secret key
Message
Message
Random
secret key
G. Vernam, U.S. patent 1310719 (filed in 1918, granted 1919) C. E. Shannon, Bell Syst. Tech. J. 28, 656 (1949)
α | β | α  β
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
of same length as message

## Slide 6: A (very) brief history of cryptography
 |  |  |  |  | Broken? |  | 
Monoalphabetic cipher |  | invented ~50 BC (J. Caesar) |  |  | ~850 (Al-Kindi) |  | 
Nomenclators (code books) |  | ~1400 – ~1800 |  |  |  |  | 
Polyalphabetic (Vigenère) |  | 1553 – ~1900 |  |  | 1863 (F. W. Kasiski) |  | 
··· |  |  |  |  |  |  | 
One-time pad |  | invented 1918 (G. Vernam) |  |  | impossible (C. Shannon 1949) |  | 
Polyalphabetic electromechanical (Enigma, Purple, etc.) |  | 1920s – 1970s |  |  |  |  | 
··· |  |  |  |  |  |  | 
DES |  | 1977 – 2005 |  |  | 1998: 56 h (EFF) |  | 
Public-key crypto (RSA, elliptic-curve) |  |  | 1977 – |  | will be once we have q. computer (P. Shor 1994) |  | 
AES |  | 2001 – |  |  | ? |  | 
Quantum cryptography | invented 1984, in development |  |  |  |  | impossible | 
Public-key crypto (‘quantum-safe’) |  | in development |  |  | ? |  | 


## Slide 7: Encryption and key distribution
Bob
Alice
Quantum key distribution transmits secret key by sending quantum states over open channel.
RNG
Symmetric
cipher
Symmetric
cipher
Public (insecure) channel
Secret key
Secure channel
Messages
Messages
Encrypted messages

## Slide 8: Quantum key distribution (QKD)
Retained bit sequence 1 – – 1 0 0 – 1 0 0 – 1 – 0
Bob’s measurement 1 0 0 1 0 0 1 1 0 0 0 1 0 0
Bob’s detection basis
Alice’s bit sequence 1 0 1 1 0 0 1 1 0 0 1 1 1 0
Light source
Alice
Bob
Diagonal detector basis
Horizontal-vertical detector basis
Diagonal polarization filters
Horizontal-vertical polarization filters
0
0
1
1
Image reprinted from article: W. Tittel, G. Ribordy & N. Gisin, “Quantum cryptography,” Physics World, March 1998

## Slide 9: Free-space QKD
T. Schmitt-Manderbach et al., Phys. Rev. Lett. 98, 010504 (2007)

## Slide 10: Phase encoding, interferometric QKD channel
jA = 0 or π/2 : 0
Detection basis:
jB = 0 : X
jB = π/2 : Z
jA = π or 3π/2 : 1
j
A
Light
source
D
0
j
B
Alice
Bob
D
1
long
short
short
long
Transmission line

## Slide 11: Plug-and-play scheme
D. Stucki et al., New J. Phys. 4, 41 (2002)
Bob
Alice
j
A
j
B
PBS
BS
C
D0
D1
L
VOA
DL
FM
sync

## Slide 12: ID Quantique Clavis2 QKD system
Alice
Bob
Photo © 2008 Vadim Makarov. Published with approval of ID Qiantique

## Slide 13: Commercial QKD
17 km (fiber length)
14 km
4 km
www.swissquantum.com
ID Quantique Cerberis system (2010)
QKD to another node
(14 km)
QKD to another node
(4 km)
Key manager
WDMs
Classical encryptors:
L2, 2 Gbit/s
L2, 10 Gbit/s
L3 VPN, 100 Mbit/s
Photo © 2010 Vadim Makarov

## Slide 14: Trusted-node repeater
K1
QKD 1
K1
K2
QKD 2
K2
K1K2
Trusted node
User
User
K1
K1K2K2 = K1

## Slide 15: Trusted-node network
M. Sasaki et al., Opt. Express 19, 10387 (2011)

## Slide 16
Q. Zhang, talk at QCrypt 2014

## Slide 17: One repeater of Chinese backbone quantum key distribution line (2000 km Beijing–Shanghai, consisting of a chain of 32 such trusted repeaters)
Photo © 2016 Vadim Makarov

## Slide 18: Customers of the Chinese quantum key distribution network (upper three rings), component suppliers and developers (lower three rings)
Photo © 2016 Vadim Makarov

## Slide 19: Quantum cryptography system with secure videotelephone made by QuantumCTek (China)
Photo © 2016 Vadim Makarov

## Slide 20: Shanghai control center of the Chinese quantum key distribution network and satellite
Photo © 2016 Vadim Makarov

## Slide 21
Video ©2012 IQC / group of T. Jennewein

## Slide 22: Quantum communication primitives
 | Advantages over classical primitives: |  | 
 | Unconditionally secure? | Less resources? | Other quantum advantages?
Key distribution |  |  | 
Secret sharing |  |  | 
Digital signatures |  |  | 
Superdense coding |  |  | 
Fingerprinting |  |  | 
Oblivious transfer | Impossible |  | 
Bit commitment | Impossible |  | 
Coin-tossing |  |  | 
Cloud computing |  |  | 
Bell inequality testing | (no classical equivalent) |  | 
Teleportation |  |  | 
Entanglement swapping |  |  | 
Random number generators |  |  | 

## Slide 23: Security model of QKD
Alice
Bob
Secret key rate
0
0.11
0
1
QBER
R
.Laws of physics & Model of equipment
Security proof

## Slide 24: Security model of QKD
.Laws of physics & Model of equipment
Security proof
.Laws of physics & Model of equipment
Security proof
Hack
Integrate imperfection into security model

## Slide 27: Today’s digital
Bus
Memory
Software
Bus
Signal proc.
DAC
Amplifier
Crypto module
Crypto module
Optical line
Quantum bus, computer, memory...
Crypto module
vs. quantum
[vs. future]

## Slide 28: True randomness?
ONE ONE ONE
ONE ONE ONE
ONE ONE ONE
Quantis
RNG
FPGA
Phase modulator in Bob
id Quantique Clavis2 (2008)
V/2
0
OK

## Slide 29: True randomness?
Quantis
RNG
FPGA
Phase modulator in Bob
Issue reported patched in 2010
Bob:
Alice:
id Quantique Clavis2 (2008)
V/2
0

## Slide 30: Do we trust the manufacturer?
Quantis RNG
*
Clicks
processed
Random
stream
Quantis RNG, Trojan-horsed :)
*
Clicks
processed
Random
stream
Switch
Memory with
pre-recorded
random
sequence
Many components in QKD system can be Trojan-horsed:
– access to secret information
– electrical power
– way to communicate outside or compromise security

## Slide 31: ID Quantique Clavis2 QKD system
Alice
Bob
Photo © 2008 Vadim Makarov. Published with approval of ID Qiantique

## Slide 32: Double clicks
N. Lütkenhaus, Phys. Rev. A 59, 3301 (1999)
T. Tsurumaru & K. Tamaki, Phys. Rev. A 78, 032302 (2008)
– occur naturally because of detector dark counts, multi-photon pulses...
Discard them?
Proper treatment for double clicks: assign a random bit value.
Intercept-resend attack... with a twist:
Bob´
Alice´
Eve
100
photons
Alice
Bob:
Detects in
Eve’s basis:
single click
Detects in
conjugate basis:
double click,
discarded

## Slide 33: Trojan-horse attack
Alice
Line
Attenuator
Alice’s PC
Eve’s equipment
Phase modulator
– interrogating Alice’s phase modulator with powerful external pulses (can give Eve bit values directly)

## Slide 34: Trojan-horse attack experiment
Laser
4% reflection
Vmod
OTDR
Out
In
Fine length adjustment
to get L1 = L2
L2
L1
Received OTDR pulse
Vmod, V
4.1
8.2
0
Variable attenuator
Alice
Phase modulator
Eve
A. Vakhitov et al., J. Mod. Opt. 48, 2023 (2001)

## Slide 35: Artem Vakhitov tunes up Eve’s setup
Photo © 2000 Vadim Makarov

## Slide 36: Trojan-horse attack for plug-and-play system
N. Gisin et al., Phys. Rev. A 73, 022320 (2006)
Alice
Bob
Eve gets back one photon  in principle, extracts 100% information

## Slide 37
End of lecture 3

## Slide 38
Implementation of quantum communication: Lecture 4
Vadim Makarov www.vad1.com/lab
Course QIC 891, University of Waterloo, August 12, 2016

## Slide 39: Outline of the rest of this course
Summary of communication security, quantum key distribution, trusted-repeater networks
Security model of QKD, side-channels in implementations
Examples of side-channel attacks, countermeasures, testing countermeasures
Conclusion & discussion
(optional) Lab visit
August 12 3

## Slide 40: Security model of quantum cryptography
.Laws of physics & Model of equipment
Security proof
Hack
Integrate imperfection into security model
Crypto module
Optical line
Today’s technology

## Slide 41: Countermeasures?
D. Stucki et al., New J. Phys. 4, 41 (2002)
Bob
Alice
j
A
j
B
PBS
BS
C
D0
D1
L
VOA
DL
FM
sync

## Slide 42: Countermeasures for plug-and-play system
Bob
Alice
j
A
j
B
PBS
BS
C
D0
D1
L
VOA
DL
FM
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015)
1. Pulse-energy-monitoring detector
2. Narrowpass
(1 nm) filter
None (one consequence: SARG protocol may be insecure)
N. Jain et al., New J. Phys. 16, 123030 (2014)
sync

## Slide 43: Trojan-horse attack on Bob
Bob
j
B
PBS
BS
C
D0
D1
L
N. Jain et al., New J. Phys. 16, 123030 (2014)
Bob
j
B
PBS
BS
C
D0
D1
L
 −50 dB
−57 dB
4 photons
2106 photons
readout
j
B

## Slide 44: Example of vulnerability and countermeasures
Photon-number-splitting attack
C. Bennett, F. Bessette, G. Brassard, L. Salvail, J. Smolin, J. Cryptology 5, 3 (1992)
G. Brassard, N. Lütkenhaus, T. Mor, B. C. Sanders, Phys. Rev. Lett. 85, 1330 (2000)
N. Lütkenhaus, Phys. Rev. A 61, 052304 (2000)
S. Félix, N. Gisin, A. Stefanov, H. Zbinden, J. Mod. Opt. 48, 2009 (2001)
N. Lütkenhaus, M. Jahma, New J. Phys. 4, 44 (2002)
Decoy-state protocol
W.-Y. Hwang, Phys. Rev. Lett. 91, 057901 (2003)
SARG04 protocol
V. Scarani, A. Acín, G. Ribordy, N. Gisin, Phys. Rev. Lett. 92, 057901 (2004)
Distributed-phase-reference protocols
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. Lett. 89, 037902 (2002)
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. A. 68, 022317 (2003)
N. Gisin, G. Ribordy, H. Zbinden, D. Stucki, N. Brunner, V. Scarani, arXiv:quant-ph/0411022v1 (2004)
Laser
Attenuator

## Slide 45: Differential-phase-shift QKD
Review: K. Inoue, IEEE J. Sel. Top. Quantum Electron. 21, 6600207 (2015)
Bob
Intercept-resend attack

## Slide 46
Attack | Target component | Tested system
Laser damage | any | ID Quantique, research system
V. Makarov et al., arXiv:1510.03148 |  | 
Spatial efficiency mismatch | receiver optics | research system
M Rau et al., IEEE J. Quantum Electron. 21, 6600905 (2015); S. Sajeed et al., Phys. Rev. A 91, 062301 (2015) |  | 
Pulse energy calibration | classical watchdog detector | ID Quantique
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015) |  | 
Trojan-horse | phase modulator in Alice | SeQureNet
I. Khan et al., presentation at QCrypt (2014) |  | 
Trojan-horse | phase modulator in Bob | ID Quantique*
N. Jain et al., New J. Phys. 16, 123030 (2014) |  | 
Detector saturation | homodyne detector | SeQureNet
H. Qin, R. Kumar, R. Alleaume, Proc. SPIE 88990N (2013) |  | 
Shot-noise calibration | classical sync detector | SeQureNet
P. Jouguet, S. Kunz-Jacques, E. Diamanti, Phys. Rev. A 87, 062313 (2013) |  | 
Wavelength-selected PNS | intensity modulator | (theory)
M.-S. Jiang, S.-H. Sun, C.-Y. Li, L.-M. Liang, Phys. Rev. A 86, 032310 (2012) |  | 
Multi-wavelength | beamsplitter | research system
H.-W. Li et al., Phys. Rev. A 84, 062308 (2011) |  | 
Deadtime | single-photon detector | research system
H. Weier et al., New J. Phys. 13, 073024 (2011) |  | 
Channel calibration | single-photon detector | ID Quantique
N. Jain et al., Phys. Rev. Lett. 107, 110501 (2011) |  | 
Faraday-mirror | Faraday mirror | (theory)
S.-H. Sun, M.-S. Jiang, L.-M. Liang, Phys. Rev. A 83, 062331 (2011) |  | 
Detector control | single-photon detector | ID Quantique, MagiQ, research system
I. Gerhardt et al., Nat. Commun. 2, 349 (2011); L. Lydersen et al., Nat. Photonics 4, 686 (2010) |  | 
* Attack did not break security of the tested system, but may be applicable to a different implementation. |  | 

## Slide 47: Attack example: avalanche photodetectors (APDs)
Ith
I
V
Linear mode
Geiger mode
Single photon
Breakdown
voltage Vbr
Popt
I
Quenching
Ith
Pth

## Slide 48: Faked-state attack in APD linear mode
Eve
L. Lydersen, C. Wiechers, C. Wittmann, D. Elser, J. Skaar, V. Makarov, Nat. Photonics 4, 686 (2010)
.Bob´
Bob
Bright
state
Identical bases & bit values
Classical post-processing
Listen, do same,
get same final key
.Alice´
Alice
Bob chooses same basis as Eve:
Bob chooses different basis:
“1
”
“0
”
t
t
I
th
I
th
t
t
I
th
I
th
I
0
I
1
I
0
I
1
“0”
“1
”
Click!

## Slide 49: Blinding APD with bright light
VAPD
Vbr
Vbias
t
0
Detector blind!
Zero dark count rate
Bias to APD
(Vbias)
VHV  40 V
Rbias
L. Lydersen, C. Wiechers, C. Wittmann, D. Elser, J. Skaar, V. Makarov, Nat. Photonics 4, 686 (2010)
No light
Eve applies CW light
0
0.5
1
1.5
2
-10
0
10
20
30
Logic 0
Logic 1
Time, ns
-10
0
10
20
30
Time, ns
t
647 W
t
808 W
(never clicks)
(always clicks)
Input
illumination,
mW
Detector
output
ID Quantique
Clavis2

## Slide 50: Proposed full eavesdropper
Basis
amplifier
Optical
Detection result
Bob´
Eve
Bob
Alice
Bit in
Basis
Alice´
Blinding laser

## Slide 51: Eavesdropping 100% key on installed QKD line on campus of the National University of Singapore, July 4–5, 2009
S12
290 m of fiber
Alice
Bob
Eve
S15
S14
S13
Image © 2009 DigitalGlobe
I. Gerhardt, Q. Liu et al., Nat. Commun. 2, 349 (2011)

## Slide 52: Countermeasures to detector attacks
Alice
Charlie (untrusted)
Bob
EPR
BSM
EPR
EPR
H.-K. Lo, M. Curty, B. Qi, Phys. Rev. Lett. 108, 130503 (2012)
1st experimental demonstration, over 18 km fiber: A. Rubenok et al., arXiv:1204.0738v2
Measurement-device-independent QKD
BSM
RNG
RNG
Mod.
Mod.
Photon
source
Photon
source

## Slide 53: Industrial countermeasure (ID Quantique)
A. Huang et al., arXiv:1601.00993
Lim et al. upload a preprint about countermeasure arXiv:1408.6398
Report about detector blinding attack sent to IDQ
IDQ applies for a patent on randomization of detector efficiency as a countermeasure
Implementation of countermeasure delivered by IDQ to our lab (firmware update for Clavis2)
Testing report sent to IDQ proposing a modified attack that works
First commercial Clavis1 system is shipped to a customer
Testing report sent to IDQ showing full implementation of
countermeasure to be unreliable

## Slide 54: Randomly varying detector efficiency
M. Legre, G. Robordy, Intl. patent appl. WO 2012/046135 A2 (filed in 2010)
VAPD
Click
Click
VAPD
Click
Click
Alarm!

## Slide 55: Oscillograms at comparator input
A. Huang et al., arXiv:1601.00993

## Slide 56: Anqi Huang tests countermeasure in Clavis2
Photo © 2015 Vadim Makarov

## Slide 57
Lesson 1. Industry needs implementation standards, certification and testing standards.
Once equipment is tested and certified, end of story?
Can Eve modify equipment after installation?
Crypto module
Optical line

## Slide 58: Efficiency mismatch in QKD receiver
S. Sajeed et al., Phys. Rev. A 91, 062301 (2015)
V. Makarov et al., arXiv:1510.03148

## Slide 59
0
1 mm
3.6 W, 810 nm laser
Thorlabs P20S pinhole
13 μm thick stainless steel
* Sound was added later

## Slide 60
0
1 mm
3.6 W, 810 nm laser
Thorlabs P20S pinhole
13 μm thick stainless steel
* Sound was added later

## Slide 61: Detector efficiency with laser-damaged pinhole
V. Makarov et al., arXiv:1510.03148

## Slide 62: Can we eavesdrop on commercial systems?
ID Quantique’s Cerberis:
Dual key agreement
Photo © 2010 Vadim Makarov
QKD
QKD
PKI
PKI
Symmetric
cipher
Symmetric
cipher
RSA-2048
BB84
AES-256
Key
Key

## Slide 63: Kerckhoffs’ principle
Il faut qu’il n’exige pas le secret, et qu’il puisse sans inconvénient tomber entre les mains de l’ennemi
A. Kerckhoffs, J. des Sciences Militaires IX, 5 (1883)
Everything about the system that is not explicitly secret is known to the enemy
Bob
Alice
Future technology
characteristics known
characteristics known

## Slide 64: Eavesdropping in real life?
Bob
Alice
Future technology
characteristics known
characteristics known
Bob
Alice
Implemented
characteristics measured
characteristics measured
I. Gerhardt et al., Nat. Commun. 2, 349 (2011)
Bob
Alice
Today’s technology
(modeled)
characteristics measured
characteristics measured
Bob
Alice
Implemented
no access
no access
Not yet :)
Bob
Alice
Future technology
characteristics known
characteristics known
Many papers
Future technology
Many papers

## Slide 65: Conclusion
Physics promises unbreakable cryptography, but implementing it with our rudimentary quantum technology is a research challenge.

## Slide 66: Suggested reading
Introduction to detector attacks and MDI-QKD
H.-K. Lo, M. Curty, K. Tamaki, Nat. Photonics 8, 595 (2014), 10 pages
Review of more hacking techniques
N. Jain et al., Contemp. Phys. 57, 366 (2016), 22 pages
Reviews are incomplete. If you are engineering a system, read original literature (or ask for my expert advice).