## Slide 1
Challenges to physical security of
today’s quantum technologies
Vadim Makarov www.vad1.com/lab
Tutorial at QCrypt, September 12-16, 2016

## Slide 2: A (very) brief history of cryptography
 |  |  |  |  | Broken? |  | 
Monoalphabetic cipher |  | invented ~50 BC (J. Caesar) |  |  | ~850 (Al-Kindi) |  | 
Nomenclators (code books) |  | ~1400 – ~1800 |  |  |  |  | 
Polyalphabetic (Vigenère) |  | 1553 – ~1900 |  |  | 1863 (F. W. Kasiski) |  | 
··· |  |  |  |  |  |  | 
One-time pad |  | invented 1918 (G. Vernam) |  |  | impossible (C. Shannon 1949) |  | 
Polyalphabetic electromechanical (Enigma, Purple, etc.) |  | 1920s – 1970s |  |  |  |  | 
··· |  |  |  |  |  |  | 
DES |  | 1977 – 2005 |  |  | 1998: 56 h (EFF) |  | 
Public-key crypto (RSA, elliptic-curve) |  |  | 1977 – |  | will be once we have q. computer (P. Shor 1994) |  | 
AES |  | 2001 – |  |  | ? |  | 
Quantum cryptography | invented 1984, in development |  |  |  |  | impossible | 
Public-key crypto (‘quantum-safe’) |  | in development |  |  | ? |  | 
 |  |  |  |  | Broken? |  | 
Monoalphabetic cipher |  | invented ~50 BC (J. Caesar) |  |  | ~850 (Al-Kindi) |  | 
Nomenclators (code books) |  | ~1400 – ~1800 |  |  |  |  | 
Polyalphabetic (Vigenère) |  | 1553 – ~1900 |  |  | 1863 (F. W. Kasiski) |  | 
··· |  |  |  |  |  |  | 
Polyalphabetic electromechanical (Enigma, Purple, etc.) |  | 1920s – 1970s |  |  |  |  | 
··· |  |  |  |  |  |  | 
DES |  | 1977 – 2005 |  |  | 1998: 56 h (EFF) |  | 
Public-key crypto (RSA, elliptic-curve) |  |  | 1977 – |  | will be once we have q. computer (P. Shor 1994) |  | 
AES |  | 2001 – |  |  | ? |  | 
Public-key crypto (‘quantum-safe’) |  | in development |  |  | ? |  | 


## Slide 3: Security model of QKD
Alice
Bob
Secret key rate
0
0.11
0
1
QBER
R
.Laws of physics & Model of equipment
Security proof

## Slide 4: Security model of QKD
.Laws of physics & Model of equipment
Security proof
.Laws of physics & Model of equipment
Security proof
Hack
Integrate imperfection into security model

## Slide 5
Attack | Target component | Tested system
Laser damage | any | ID Quantique, research system
V. Makarov et al., arXiv:1510.03148 |  | 
Spatial efficiency mismatch | receiver optics | research system
M Rau et al., IEEE J. Quantum Electron. 21, 6600905 (2015); S. Sajeed et al., Phys. Rev. A 91, 062301 (2015) |  | 
Pulse energy calibration | classical watchdog detector | ID Quantique
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015) |  | 
Trojan-horse | phase modulator in Alice | SeQureNet
I. Khan et al., presentation at QCrypt (2014) |  | 
Trojan-horse | phase modulator in Bob | ID Quantique*
N. Jain et al., New J. Phys. 16, 123030 (2014) |  | 
Detector saturation | homodyne detector | SeQureNet
H. Qin, R. Kumar, R. Alleaume, Proc. SPIE 88990N (2013) |  | 
Shot-noise calibration | classical sync detector | SeQureNet
P. Jouguet, S. Kunz-Jacques, E. Diamanti, Phys. Rev. A 87, 062313 (2013) |  | 
Wavelength-selected PNS | intensity modulator | (theory)
M.-S. Jiang, S.-H. Sun, C.-Y. Li, L.-M. Liang, Phys. Rev. A 86, 032310 (2012) |  | 
Multi-wavelength | beamsplitter | research system
H.-W. Li et al., Phys. Rev. A 84, 062308 (2011) |  | 
Deadtime | single-photon detector | research system
H. Weier et al., New J. Phys. 13, 073024 (2011) |  | 
Channel calibration | single-photon detector | ID Quantique
N. Jain et al., Phys. Rev. Lett. 107, 110501 (2011) |  | 
Faraday-mirror | Faraday mirror | (theory)
S.-H. Sun, M.-S. Jiang, L.-M. Liang, Phys. Rev. A 83, 062331 (2011) |  | 
Detector control | single-photon detector | ID Quantique, MagiQ, research system
I. Gerhardt et al., Nat. Commun. 2, 349 (2011); L. Lydersen et al., Nat. Photonics 4, 686 (2010) |  | 
* Attack did not break security of the tested system, but may be applicable to a different implementation. |  | 

## Slide 8: Today’s digital
Bus
Memory
Software
Bus
Signal proc.
DAC
Amplifier
Crypto module
Crypto module
Optical line
Quantum bus, computer, memory...
Crypto module
vs. quantum
[vs. future quantum]

## Slide 9: True randomness?
ONE ONE ONE
ONE ONE ONE
ONE ONE ONE
Quantis
RNG
FPGA
Phase modulator in Bob
id Quantique Clavis2 (2008)
V/2
0
OK

## Slide 10: True randomness?
Quantis
RNG
FPGA
Phase modulator in Bob
Issue reported patched in 2010
Bob:
Alice:
id Quantique Clavis2 (2008)
V/2
0

## Slide 11: Do we trust the manufacturer?
Quantis RNG
*
Clicks
processed
Random
stream
Quantis RNG, Trojan-horsed :)
*
Clicks
processed
Random
stream
Switch
Memory with
pre-recorded
random
sequence
Many components in QKD system can be Trojan-horsed:
– access to secret information
– electrical power
– way to communicate outside or compromise security

## Slide 12: ID Quantique Clavis2 QKD system
Alice
Bob
Photo © 2008 Vadim Makarov. Published with approval of ID Qiantique

## Slide 13: Double clicks
N. Lütkenhaus, Phys. Rev. A 59, 3301 (1999)
T. Tsurumaru & K. Tamaki, Phys. Rev. A 78, 032302 (2008)
– occur naturally because of detector dark counts, multi-photon pulses...
Discard them?
Proper treatment for double clicks: assign a random bit value.
Intercept-resend attack... with a twist:
Bob´
Alice´
Eve
100
photons
Alice
Bob:
Detects in
Eve’s basis:
single click
Detects in
conjugate basis:
double click,
discarded

## Slide 14: Trojan-horse attack
Alice
Line
Attenuator
Alice’s PC
Eve’s equipment
Phase modulator
– interrogating Alice’s phase modulator with powerful external pulses (can give Eve bit values directly)

## Slide 15: Trojan-horse attack experiment
Laser
4% reflection
Vmod
OTDR
Out
In
Fine length adjustment
to get L1 = L2
L2
L1
Received OTDR pulse
Vmod, V
4.1
8.2
0
Variable attenuator
Alice
Phase modulator
Eve
A. Vakhitov et al., J. Mod. Opt. 48, 2023 (2001)

## Slide 16: Artem Vakhitov tunes up Eve’s setup
Photo © 2000 Vadim Makarov

## Slide 17: Trojan-horse attack for plug-and-play system
N. Gisin et al., Phys. Rev. A 73, 022320 (2006)
Alice
Bob
Eve gets back one photon  in principle, extracts 100% information

## Slide 18: Countermeasures?
D. Stucki et al., New J. Phys. 4, 41 (2002)
Bob
Alice
j
A
j
B
PBS
BS
C
D0
D1
L
VOA
DL
FM
sync

## Slide 19: Countermeasures for plug-and-play system
Bob
Alice
j
A
j
B
PBS
BS
C
D0
D1
L
VOA
DL
FM
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015)
1. Pulse-energy-monitoring detector
2. Narrowpass
(1 nm) filter
None (one consequence: SARG protocol may be insecure)
N. Jain et al., New J. Phys. 16, 123030 (2014)
sync

## Slide 20: Trojan-horse attack on Bob
Bob
j
B
PBS
BS
C
D0
D1
L
N. Jain et al., New J. Phys. 16, 123030 (2014)
Bob
j
B
PBS
BS
C
D0
D1
L
 −50 dB
−57 dB
4 photons
2106 photons
readout
j
B

## Slide 21: Trojan-horse attack on Bob
S. Sajeed et al., unpublished
Bob
j
B
PBS
BS
C
D0
D1
L
readout
j
B
1924 nm

## Slide 22: Countermeasures for plug-and-play system
Bob
Alice
j
A
j
B
PBS
BS
C
D0
D1
L
VOA
DL
FM
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015)
1. Pulse-energy-monitoring detector
2. Narrowpass
(1 nm) filter
None (one consequence: SARG protocol may be insecure)
N. Jain et al., New J. Phys. 16, 123030 (2014)
sync

## Slide 23: Pulse-energy-monitoring detector
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015)
Theory:
Implementation:

## Slide 24: Pulse-energy-monitoring detector
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015)
“Certification standard” (internal by ID Quantique):

## Slide 25: Pulse-energy-monitoring detector
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015)
Theory:
Implementation:

## Slide 26: Pulse-energy-monitoring detector
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015)
Theory:
Attack:

## Slide 27: Lesson 1. Industry needs implementation standards, certification and testing standards.
ETSI industry specification group for QKD
First security standard: Trojan-horse in one-way system
M. Lucamarini et al., Phys. Rev. X 5, 031030 (2015)
Alice
Att.


Isolator(s)
BPF
R. Alléaume et al., Proc. IEEE Globecom Workshop 2014, p. 656

## Slide 28: Example of vulnerability and countermeasures
Photon-number-splitting attack
C. Bennett, F. Bessette, G. Brassard, L. Salvail, J. Smolin, J. Cryptology 5, 3 (1992)
G. Brassard, N. Lütkenhaus, T. Mor, B. C. Sanders, Phys. Rev. Lett. 85, 1330 (2000)
N. Lütkenhaus, Phys. Rev. A 61, 052304 (2000)
S. Félix, N. Gisin, A. Stefanov, H. Zbinden, J. Mod. Opt. 48, 2009 (2001)
N. Lütkenhaus, M. Jahma, New J. Phys. 4, 44 (2002)
Decoy-state protocol
W.-Y. Hwang, Phys. Rev. Lett. 91, 057901 (2003)
SARG04 protocol
V. Scarani, A. Acín, G. Ribordy, N. Gisin, Phys. Rev. Lett. 92, 057901 (2004)
Distributed-phase-reference protocols
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. Lett. 89, 037902 (2002)
K. Inoue, E. Waks, Y. Yamamoto, Phys. Rev. A. 68, 022317 (2003)
N. Gisin, G. Ribordy, H. Zbinden, D. Stucki, N. Brunner, V. Scarani, arXiv:quant-ph/0411022v1 (2004)
Laser
Attenuator

## Slide 29: Attack example: avalanche photodetectors (APDs)
Ith
I
V
Linear mode
Geiger mode
Single photon
Breakdown
voltage Vbr
Popt
I
Quenching
Ith
Pth

## Slide 30: Detector deadtime attack
H. Weier et al., New J. Phys. 13, 073024 (2011)
BS
/2
PBS
PBS
Bob
Alice
Eve
 N
Time
Sensitivity
Deadtime

## Slide 31: Attack example: avalanche photodetectors (APDs)
Ith
I
V
Linear mode
Geiger mode
Single photon
Breakdown
voltage Vbr
Popt
I
Quenching
Ith
Pth

## Slide 32: Faked-state attack in APD linear mode
Eve
L. Lydersen, C. Wiechers, C. Wittmann, D. Elser, J. Skaar, V. Makarov, Nat. Photonics 4, 686 (2010)
.Bob´
Bob
Bright
state
Identical bases & bit values
Classical post-processing
Listen, do same,
get same final key
.Alice´
Alice
Bob chooses same basis as Eve:
Bob chooses different basis:
“1
”
“0
”
t
t
I
th
I
th
t
t
I
th
I
th
I
0
I
1
I
0
I
1
“0”
“1
”
Click!

## Slide 33: Blinding APD with bright light
VAPD
Vbr
Vbias
t
0
Detector blind!
Zero dark count rate
Bias to APD
(Vbias)
VHV  40 V
Rbias
L. Lydersen, C. Wiechers, C. Wittmann, D. Elser, J. Skaar, V. Makarov, Nat. Photonics 4, 686 (2010)
No light
Eve applies CW light
0
0.5
1
1.5
2
-10
0
10
20
30
Logic 0
Logic 1
Time, ns
-10
0
10
20
30
Time, ns
t
647 W
t
808 W
(never clicks)
(always clicks)
Input
illumination,
mW
Detector
output
ID Quantique
Clavis2

## Slide 34: Proposed full eavesdropper
Basis
amplifier
Optical
Detection result
Bob´
Eve
Bob
Alice
Bit in
Basis
Alice´
Blinding laser
Note: Intercept-resend always breaks QKD security
M. Curty, M. Lewenstein, N. Lütkenhaus, Phys. Rev. Lett. 92, 217903 (2004)

## Slide 35: Eavesdropping 100% key on installed QKD line on campus of the National University of Singapore, July 4–5, 2009
S12
290 m of fiber
Alice
Bob
Eve
S15
S14
S13
Image © 2009 DigitalGlobe
I. Gerhardt, Q. Liu et al., Nat. Commun. 2, 349 (2011)

## Slide 36: Perfect countermeasure to detector attacks
H.-K. Lo, M. Curty, B. Qi, Phys. Rev. Lett. 108, 130503 (2012)
Measurement-device-independent QKD
Alice
Charlie (untrusted)
Bob
Bell-state measurement
RNG
RNG
Mod.
Mod.
Photon
source
Photon
source

## Slide 37: Industrial countermeasure (ID Quantique)
A. Huang et al., arXiv:1601.00993
Lim et al. upload a preprint about countermeasure arXiv:1408.6398
Report about detector blinding attack sent to IDQ
IDQ applies for a patent on randomization of detector efficiency as a countermeasure
Implementation of countermeasure delivered by IDQ to our lab (firmware update for Clavis2)
Testing report sent to IDQ proposing a modified attack that works
First commercial Clavis1 system is shipped to a customer
Testing report sent to IDQ showing full implementation of
countermeasure to be unreliable

## Slide 38: Once equipment is tested and certified, end of story?
Can Eve modify equipment after installation?
Laser damage
Crypto module
Optical line
V. Makarov et al., arXiv:1510.03148

## Slide 39: Can we eavesdrop on commercial systems?
ID Quantique’s Cerberis:
Dual key agreement
Photo © 2010 Vadim Makarov
QKD
QKD
PKI
PKI
Symmetric
cipher
Symmetric
cipher
RSA-2048
BB84
AES-256
Key
Key

## Slide 40: Kerckhoffs’ principle
Il faut qu’il n’exige pas le secret, et qu’il puisse sans inconvénient tomber entre les mains de l’ennemi
A. Kerckhoffs, J. des Sciences Militaires 9, 5 (1883)
Everything about the system that is not explicitly secret is known to the enemy
Bob
Alice
Future technology
characteristics known
characteristics known

## Slide 41: Eavesdropping in real life?
Bob
Alice
Future technology
characteristics known
characteristics known
Bob
Alice
Implemented
characteristics measured
characteristics measured
I. Gerhardt et al., Nat. Commun. 2, 349 (2011)
Bob
Alice
Today’s technology
(modeled)
characteristics measured
characteristics measured
Bob
Alice
Implemented
no access
no access
Not yet :)
Bob
Alice
Future technology
characteristics known
characteristics known
Many papers
Future technology
Many papers

## Slide 42: What about device-independent protocols?
J. Barrett, R. Colbeck, A. Kent, Phys. Rev. Lett. 110, 010503 (2013)
V. Makarov et al., arXiv:1510.03148
Alice
Bob
Assumptions:
1. No information-leakage channels
2. No memory

Eve

## Slide 43: Conclusion
Physics promises unbreakable cryptography, but implementing it with our rudimentary quantum technology is a research challenge.

## Slide 44: Suggested reading
Introduction to detector attacks and MDI-QKD
H.-K. Lo, M. Curty, K. Tamaki, Nat. Photonics 8, 595 (2014), 10 pages
Review of more hacking techniques
N. Jain et al., Contemp. Phys. 57, 366 (2016), 22 pages
Reviews are incomplete. If you are engineering a system, read original literature (or ask for my expert advice).

## Slide 45: Informal security evaluation
Only industrial designs
NDA, full access to engineering documentation
Team of experts :)
Identify all known potential vulnerabilities in optics and electronics (Q1–4)
Stage I: Initial analysis of documentation
Stage II: Lab testing
Photo © 2016 Vadim Makarov

## Slide 46: Security analysis layers in quantum communication
Q7. Installation and maintenance procedures
Q6. Application interface
Q5. Post-processing (e.g., for QKD: sifting, error correction, privacy amplification, authentication)
Q4. Operation cycle (state machine)
Q3. Driver and calibration algorithms
Q2. Analog electronics interface
Q1. Optics

## Slide 47: Example of initial analysis report