## Slide 1
Talk at IT nights, Innopolis, 1–2 August 2019
Quantum cryptography
Vadim Makarov
Image: street mural in Bucharest (fragment)
© 2013 Obie Platon, Irlo, Pisica Pătrată, Last, Spesh, Lumin

## Slide 2: A (very) brief history of cryptography
 |  |  |  |  | Broken? |  | 
Monoalphabetic cipher |  | invented ~50 BC (J. Caesar) |  |  | ~850 (Al-Kindi) |  | 
Nomenclators (code books) |  | ~1400 – ~1800 |  |  |  |  | 
Polyalphabetic (Vigenère) |  | 1553 – ~1900 |  |  | 1863 (F. W. Kasiski) |  | 
··· |  |  |  |  |  |  | 
Polyalphabetic electromechanical (Enigma, Purple, etc.) |  | 1920s – 1970s |  |  |  |  | 
··· |  |  |  |  |  |  | 
DES |  | 1977 – 2005 |  |  | 1998: 56 h (EFF) |  | 
Public-key crypto (RSA, elliptic-curve) |  |  | 1977 – |  | will be once we have q. computer (P. Shor 1994) |  | 
AES |  | 2001 – |  |  | ? |  | 
Public-key crypto (‘quantum-safe’) |  | in development |  |  | ? |  | 

## Slide 3: Breaking cryptography retroactively
z (time to build large quantum computer)
y (re-tool infrastructure)
x (encryption needs be secure)
Time
M. Mosca, http://eprint.iacr.org/2015/1075
Mosca theorem
If x + y > z, then worry.
Encrypt
Decrypt
Store copy
Decrypt
In future:
Photo © 2013 AP / Rick Bowmer

## Slide 4: A (very) brief history of cryptography
 |  |  |  |  | Broken? |  | 
Monoalphabetic cipher |  | invented ~50 BC (J. Caesar) |  |  | ~850 (Al-Kindi) |  | 
Nomenclators (code books) |  | ~1400 – ~1800 |  |  |  |  | 
Polyalphabetic (Vigenère) |  | 1553 – ~1900 |  |  | 1863 (F. W. Kasiski) |  | 
··· |  |  |  |  |  |  | 
One-time pad |  | invented 1918 (G. Vernam) |  |  | impossible (C. Shannon 1949) |  | 
Polyalphabetic electromechanical (Enigma, Purple, etc.) |  | 1920s – 1970s |  |  |  |  | 
··· |  |  |  |  |  |  | 
DES |  | 1977 – 2005 |  |  | 1998: 56 h (EFF) |  | 
Public-key crypto (RSA, elliptic-curve) |  |  | 1977 – |  | will be once we have q. computer (P. Shor 1994) |  | 
AES |  | 2001 – |  |  | ? |  | 
Quantum cryptography | invented 1984, in development |  |  |  |  | impossible | 
Public-key crypto (‘quantum-safe’) |  | in development |  |  | ? |  | 
 |  |  |  |  | Broken? |  | 
Monoalphabetic cipher |  | invented ~50 BC (J. Caesar) |  |  | ~850 (Al-Kindi) |  | 
Nomenclators (code books) |  | ~1400 – ~1800 |  |  |  |  | 
Polyalphabetic (Vigenère) |  | 1553 – ~1900 |  |  | 1863 (F. W. Kasiski) |  | 
··· |  |  |  |  |  |  | 
Polyalphabetic electromechanical (Enigma, Purple, etc.) |  | 1920s – 1970s |  |  |  |  | 
··· |  |  |  |  |  |  | 
DES |  | 1977 – 2005 |  |  | 1998: 56 h (EFF) |  | 
Public-key crypto (RSA, elliptic-curve) |  |  | 1977 – |  | will be once we have q. computer (P. Shor 1994) |  | 
AES |  | 2001 – |  |  | ? |  | 
Public-key crypto (‘quantum-safe’) |  | in development |  |  | ? |  | 


## Slide 5: One-time pad
Bob
Alice
Random
secret key
Message
Message
Random
secret key
G. Vernam, U.S. patent 1310719 (filed in 1918, granted 1919) C. E. Shannon, Bell Syst. Tech. J. 28, 656 (1949)
α | β | α  β
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
of same length as message

## Slide 6: A (very) brief history of cryptography
 |  |  |  |  | Broken? |  | 
Monoalphabetic cipher |  | invented ~50 BC (J. Caesar) |  |  | ~850 (Al-Kindi) |  | 
Nomenclators (code books) |  | ~1400 – ~1800 |  |  |  |  | 
Polyalphabetic (Vigenère) |  | 1553 – ~1900 |  |  | 1863 (F. W. Kasiski) |  | 
··· |  |  |  |  |  |  | 
One-time pad |  | invented 1918 (G. Vernam) |  |  | impossible (C. Shannon 1949) |  | 
Polyalphabetic electromechanical (Enigma, Purple, etc.) |  | 1920s – 1970s |  |  |  |  | 
··· |  |  |  |  |  |  | 
DES |  | 1977 – 2005 |  |  | 1998: 56 h (EFF) |  | 
Public-key crypto (RSA, elliptic-curve) |  |  | 1977 – |  | will be once we have q. computer (P. Shor 1994) |  | 
AES |  | 2001 – |  |  | ? |  | 
Quantum cryptography | invented 1984, in development |  |  |  |  | impossible | 
Public-key crypto (‘quantum-safe’) |  | in development |  |  | ? |  | 


## Slide 7: Key distribution for encryption
Bob
Alice
Quantum key distribution transmits secret key by sending quantum states over open channel.
Public (insecure) channel
Secret key
Secure channel
Messages
Messages
Encrypted messages
RNG
Symmetric
cipher
Symmetric
cipher

## Slide 8: Quantum key distribution (QKD)
Prepares
photons
Measures
photons
Bob
Alice
(0), (1)
(0), (1)
or ?
Eavesdropping
introduces errors
C. H. Bennett, G. Brassard (1984)

## Slide 9: Post-processing in QKD
Raw photon detection data
Bob
Alice
C. H. Bennett et al., J. Cryptology 5, 3 (1992); N. Lütkenhaus, Phys. Rev. A 59, 3301 (1999)
Classical channel (e.g., internet)
Sifting (discard bits Bob failed to detect or detected in incompatible basis)
Error correction
Secret key rate estimation
Privacy amplification (compress key using a hash function)
Authentication Alice–Bob
Secret key
error rate
0
0.11
0
1
error rate
R
small fraction
1st time: initial short key, or
public-key infrastructure
R

## Slide 10: Commercial QKD
17 km (fiber length)
14 km
4 km
www.swissquantum.com
ID Quantique Cerberis system (2010)
QKD to another node
(14 km)
QKD to another node
(4 km)
Key manager
WDMs
Classical encryptors:
L2, 2 Gbit/s
L2, 10 Gbit/s
L3 VPN, 100 Mbit/s
Photo © 2010 Vadim Makarov

## Slide 11: Trusted-node network
M. Sasaki et al., Opt. Express 19, 10387 (2011)

## Slide 12: Shanghai control center of the Chinese quantum key distribution network and satellite
Photo © 2016 Vadim Makarov

## Slide 13
Global quantum key distribution
Video ©2012 IQC / group of T. Jennewein

## Slide 14
Video ©2012 IQC / group of T. Jennewein

## Slide 15: Chinese quantum satellite Micius (launched 2016)
Bell test over 1200 km
Satellite-to-ground QKD at 1 kbit/s
Quantum teleportation over 1400 km
J. Yin et al., Science 356, 1140 (2017)
S.-K. Liao et al., Nature 549, 43 (2017)
J.-G. Ren et al., Nature 549, 70 (2017)
Graphics © 2017 C. Bickel / Science

## Slide 16: Certification of cryptographic tools
Government
Legal requirements
Approval
Certificate
System
Engineering documentation
Sale
Accredited lab
Manufacturer
Customer
National security agency

## Slide 17: Certification of cryptographic tools
Government
Legal requirements
Approval
Certificate
System
Engineering documentation
Sale
Accredited lab
Manufacturer
Customer
Russia: optional for commercial uses
National security agency

## Slide 19: Implementation security of quantum communications
.Laws of physics & Model of equipment
Security proof
Hack
Integrate imperfection into security model
Formal certification: we need
standards and labs ecosystem

## Slide 20
Attack | Target component | Tested system
Distinguishability of decoy states | laser in Alice | 3 research systems
A. Huang et al., Phys. Rev. A 98, 012330 (2018) |  | 
Intersymbol interference | intensity modulator in Alice | research system
K. Yoshino et al., poster at QCrypt (2016) |  | 
Laser damage | any | 5 commercial & 1 research systems
V. Makarov et al., Phys. Rev. A 94, 030302 (2016); A. Huang et al., poster at QCrypt (2018) |  | 
Spatial efficiency mismatch | receiver optics | 2 research systems
M. Rau et al., IEEE J. Sel. Top. Quantum Electron. 21, 6600905 (2015); S. Sajeed et al., Phys. Rev. A 91, 062301 (2015) |  | 
Pulse energy calibration | classical watchdog detector | ID Quantique
S. Sajeed et al., Phys. Rev. A 91, 032326 (2015) |  | 
Trojan-horse | phase modulator in Alice | SeQureNet
I. Khan et al., presentation at QCrypt (2014) |  | 
Trojan-horse | phase modulator in Bob | ID Quantique
N. Jain et al., New J. Phys. 16, 123030 (2014); S. Sajeed et al., Sci. Rep. 7, 8403 (2017) |  | 
Detector saturation | homodyne detector | SeQureNet
H. Qin, R. Kumar, R. Alleaume, Proc. SPIE 88990N (2013) |  | 
Shot-noise calibration | classical sync detector | SeQureNet
P. Jouguet, S. Kunz-Jacques, E. Diamanti, Phys. Rev. A 87, 062313 (2013) |  | 
Wavelength-selected PNS | intensity modulator | (theory)
M.-S. Jiang, S.-H. Sun, C.-Y. Li, L.-M. Liang, Phys. Rev. A 86, 032310 (2012) |  | 
Multi-wavelength | beamsplitter | research system
H.-W. Li et al., Phys. Rev. A 84, 062308 (2011) |  | 
Deadtime | single-photon detector | research system
H. Weier et al., New J. Phys. 13, 073024 (2011) |  | 
Channel calibration | single-photon detector | ID Quantique
N. Jain et al., Phys. Rev. Lett. 107, 110501 (2011) |  | 
Faraday-mirror | Faraday mirror | (theory)
S.-H. Sun, M.-S. Jiang, L.-M. Liang, Phys. Rev. A 83, 062331 (2011) |  | 
Detector control | single-photon detector | ID Quantique, MagiQ, research systems
I. Gerhardt et al., Nat. Commun. 2, 349 (2011); L. Lydersen et al., Nat. Photonics 4, 686 (2010) |  | 

## Slide 21
Photo © 2015 Vadim Makarov
Anqi Huang tests countermeasure in Clavis2

## Slide 22: Attacks require realtime physical access to channel
Fiber: easy
Free-space:
slightly difficult

## Slide 23: Polarization receiver for satellite
C. J. Pugh et al., Quantum Sci. Technol. 2, 024009 (2017)

## Slide 24: Polarization analyzer
J.-P. Bourgoin et al., Phys. Rev. A 92, 052339 (2015)

## Slide 25: Polarization analyzer
J.-P. Bourgoin et al., Phys. Rev. A 92, 052339 (2015)

## Slide 26: Efficiency mismatch in polarization analyzer
S. Sajeed et al., Phys. Rev. A 91, 062301 (2015)

## Slide 27: Detector efficiency without pinhole
...and with 25 μm
diameter pinhole
S. Sajeed et al., Phys. Rev. A 91, 062301 (2015)

## Slide 28: Counter-attack
V. Makarov et al., Phys. Rev. A 94, 030302 (2016)

## Slide 29
0
1 mm
3.6 W, 810 nm laser
Thorlabs P20S pinhole
13 μm thick stainless steel
* Sound was added later

## Slide 30
0
1 mm
3.6 W, 810 nm laser
Thorlabs P20S pinhole
13 μm thick stainless steel
* Sound was added later

## Slide 31: Security audit
 | System | Report | Tests
 | Clavis3 | 2016 | –2018 incomplete
 | 40 MHz system | 2016, 2018–19 | ongoing
(ООО Квантовые коммуникации) | Subcarrier scheme (A. Gleim) | 2018 | ongoing
International certification standards are being developed
Industry standards group in QKD
S. Sajeed et al., unpublished
 | New 1 GHz system | (2019) | to do

## Slide 32
Quantum communications at
A. Fedorov
(theory)
V. Makarov
(hacking)
Image from cartoon “Dobrinya and the Dragon” (Melnitsa Animation Studio, 2006)
Y. Kurochkin ( )

## Slide 33
Winter school on quantum cybersecurity
Annual. Next: 25–31 January 2020 Les Diablerets, Switzerland
2 days (executive track) + 4 days (technical track, with 4 labs)
Overview talks + quantum technologies, including QKD
Lecturers in 2019: J. Baloo, C. Bennett, G. Brassard, E. Diamanti, R. Floeter, N. Gisin, J. Hart, B. Huttner, E. Hodges, V. Makarov, M. Mosca, S. Popescu, R. Renner, F. Ruess, G. Ribordy, V. Scarani, D. Stucki, C. Williams
30 students, first-come, sells out
€3200 / €1600 executive track only
Winter sports in breaks
Organised by
www.idquantique.com/winter-school-2018
2016
International school on quantum technology
Annual. Next: early March 2020
Roza Khutor, Russia
4 days of lectures and skiing,
poster session
Tutorials on quantum sensing, computing, metrology, QKD
Lecturers in 2019: A. Akimov, V. Balykin, M. Chekhova, V. Eliseev, A. Fedyanin, A. Korolkov, L. Krivitsky, V. Makarov, A. Odinokov, O. Snigirev, S. Straupe, A. Urivsky, S. Vyatchanin, F. Zhelezko
100 students, competitive admission
€80 academic / €300 other (TBC)
4 h of pro skiing instruction
Organised by
qutes.org
2018
2019