## Slide 1
Improving security of a QKD system via an external audit
Talk at BQIT online workshop, 27–30 April 2020
Photo © 2017 Vadim Makarov / ITMO
vad1.com/lab
Quantum hacking lab
Vadim 大胡子

## Slide 2: Certification of cryptographic tools
Government
Legal requirements
Certificate
System
Engineering documentation
Sale
Accredited lab
Manufacturer
Customer
National security authority

## Slide 4: Security audit
 | System | Report | Tests
 | Clavis3 | 2016 | –2018 interrupted
 | 40 MHz | 2016, 2018–19 | ongoing
(ООО Квантовые коммуникации) | Subcarrier scheme | 2018 | ongoing
Certification standards are being drafted since 2019 in
Industry standards group in QKD
 | New 312.5 MHz system | (2020) | ongoing
S. Sajeed et al., arXiv:1909.07898

## Slide 5: Hardness against implementation imperfections
Rating | Description
C3. Solution secure | Imperfection not applicable or in security proof
C2. Solution robust | Protects against known attacks but is not in security proof
C1. Solution only partially effective | Protects adainst one attack but fails to another
C0. Insecure | Loophole confirmed, no countermeasure
CX. Not tested | Loophole suspected
S. Sajeed, P. Chaiwongkhot, A. Huang, H. Qin, V. Egorov, A. Kozubov, A. Gaidash, V. Chistiakov, A. Vasiliev, A. Gleim, V. Makarov, arXiv:1909.07898

## Slide 6: Risk evaluation
Loophole likely 1 or unlikely 0 to exist?
Exploitable with today’s 1 or future 0 technology?
Leaks major 1 or minor 0 fraction of key?
+
+
= risk
3 Very high 2 High 1 Medium 0 Low
H. Qin, A. Huang, S.-H. Sun, V. Makarov, confidential report for Quantum CTek (2019), unpublished

## Slide 7: Potential issue
 | C2017 | Q | Needed lab testing? | Initial risk eva-luation | C2020 | Status in early 2020
Detector control attack | CX | Q1–5,7 | Yes | High | C2 | Loophole experimentally confirmed, countermeasures implemented
Laser damage | CX | Q1,3 | Yes | High | C2 | Loophole experimentally confirmed in Alice, countermeasures implemented
Trojan horse | C2, C0 | Q1 | Yes | Low (Alice), High (Bob) | C2, C2 | Countermeasure developed, to be implemented
No general security proof | C0 | Q1,5 | No | High | C3 | Security proofs developed, software updated
Time-shift attack | CX | Q1–3,5 | Yes | Medium | CX | Lower priority, future work
Privacy amplification | C0 | Q5 | No | High | C3 | Correct processing implemented
Finite-key-size effects | C0 | Q5 | No | Low | C3 | Security proofs developed, software updated
Non-quantum RNG | C0 | Q5 | No | Low | C3 | Physical RNG selected, to be implemented
Intersymbol interference | CX | Q1–3 | Yes | Low | CX | Lower priority, future work
S. Sajeed, P. Chaiwongkhot, A. Huang, H. Qin, V. Egorov, A. Kozubov, A. Gaidash, V. Chistiakov, A. Vasiliev, A. Gleim, V. Makarov, arXiv:1909.07898

## Slide 8: Subcarrier-wave QKD scheme
A. V. Gleim et al., Opt. Express 24, 2619 (2016)
Att
φA
Ω
φB
Ω
Alice
Bob
ω−Ω ω ω+Ω
ω−Ω ω ω+Ω
ω−Ω ω+Ω
ω
φA = φB
ω−Ω ω+Ω
|φA− φB| = π

## Slide 9: 1. Detector control attack
V. Chistiakov et al., Opt. Express 27, 32253 (2019)
M. Elezov et al., Opt. Express 27, 30979 (2019)
Att
φA
Ω
φB
Ω
Alice
Bob
Bob´
Alice´
ID210 or
Scontel SNSPD
ω
V. Chistiakov et al., Opt. Express 27, 32253 (2019)

## Slide 10: 2. Laser damage
A. Huang et al., Phys. Rev. Appl. 13, 034017 (2020)
Att
φA
Ω
φB
Ω
Alice
Bob
FOD 5418
~ 3 W
A. Ponosova et al., unpublished
~ 10 dB reduction
1 mm
0

## Slide 11: 3. Trojan horse
Att
φA
Ω
φB
Ω
Alice
Bob
φA
φB
Patent pending

## Slide 12: 4. Lack of general security proof
Att
φA
Ω
φB
Ω
Alice
Bob
QND or manipulating reference ω
G. P. Miroshnichenko et al., Opt. Express 26, 11292 (2018)
Collective beamsplitting attack
A. Kozubov, A. Gaidash, G. Miroshnichenko, arXiv:1903.04371
A. Gaidash, A. Kozubov, G. Miroshnichenko, J. Opt. Soc. Am. B 36, B16 (2019)
A. Gaidash, A. Kozubov, G. Miroshnichenko, Physica Scr. (2019)
General proof

## Slide 13: 6. Privacy amplification
Att
φA
Ω
φB
Ω
Alice
Bob
A. Kozubov, A. Gaidash, G. Miroshnichenko, arXiv:1903.04371

## Slide 14: 7. Finite-key-size effects
Att
φA
Ω
φB
Ω
Alice
Bob
A. Kozubov, A. Gaidash, G. Miroshnichenko, arXiv:1903.04371
N

## Slide 15: 8. Non-quantum random number generator
Att
φA
Ω
φB
Ω
Alice
Bob
RNG
RNG
Q
Q
A. Ivanova et al., Nanosyst. Phys. Chem. Math. 8, 441 (2017)

## Slide 16: Potential issue
 | C2017 | Q | Needed lab testing? | Initial risk eva-luation | C2020 | Status in early 2020
Detector control attack | CX | Q1–5,7 | Yes | High | C2 | Loophole experimentally confirmed, countermeasures implemented
Laser damage | CX | Q1,3 | Yes | High | C2 | Loophole experimentally confirmed in Alice, countermeasures implemented
Trojan horse | C2, C0 | Q1 | Yes | Low (Alice), High (Bob) | C2, C2 | Countermeasure developed, to be implemented
No general security proof | C0 | Q1,5 | No | High | C3 | Security proofs developed, software updated
Time-shift attack | CX | Q1–3,5 | Yes | Medium | CX | Lower priority, future work
Privacy amplification | C0 | Q5 | No | High | C3 | Correct processing implemented
Finite-key-size effects | C0 | Q5 | No | Low | C3 | Security proofs developed, software updated
Non-quantum RNG | C0 | Q5 | No | Low | C3 | Physical RNG selected, to be implemented
Intersymbol interference | CX | Q1–3 | Yes | Low | CX | Lower priority, future work
S. Sajeed, P. Chaiwongkhot, A. Huang, H. Qin, V. Egorov, A. Kozubov, A. Gaidash, V. Chistiakov, A. Vasiliev, A. Gleim, V. Makarov, arXiv:1909.07898

## Slide 17
Photo © 2017 Vadim Makarov
+ V. Chistiakov, V. Egorov, S. Feng, A. Gaidash, A. Gleim, S. Kozlov, A. Kozubov, M. Legre, D. Li, N. Lütkenhaus, G. Ribordy, S.-H. Sun, Y. Tang, A. Vasiliev, Y. Zhao
A. Huang S. Sajeed P. Chaiwongkhot H. Qin

## Slide 18
Winter school on quantum cybersecurity
Annual. Next: January 2021 Les Diablerets, Switzerland
2 days (executive track) + 4 days (technical track, with 4 labs)
Overview talks + quantum technologies, including QKD
Lecturers in 2020: R. Alléaume, J. Baloo, G. Brassard, F. Bussières, A. Ekert, N. Gisin, V. Makarov, M. Mosca, L. Perret, S. Popescu, R. Pravahan, R. Renner, H. Riel, G. Ribordy, D. Stucki, N. Walenta, E. Wille
35 students, first-come, sells out
€3200 / €1600 executive track only
Winter sports in breaks
Organised by
Contact www.idquantique.com for registration
2016
International school on quantum technology
Annual. Next: early March 2021
Roza Khutor, Russia
5 days of lectures and skiing,
poster session, industry exhibit
Tutorials on quantum sensing, computing, metrology, QKD
Lecturers in 2020: S. Astakhov, M. Bellini, J. Biamonte, A. Bramati, E. Duplyakin, M. Fedorov, M. Genovese, P. Grangier, Z. Hradil, E. Il’ichev, N. Kolachevsky, V. Makarov, L. L. S. Soto, S. Takeuchi
100 students, competitive admission
€200
Skiing & snowboarding instruction
Organised by
qutes.org
2018
2019